| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 1/6 Ref. DB: |
| --- | --- | --- |

# Please complete and submit this ATLAS Standard Form to ATLAS RHA Coordinator (ARC),

# at least 2 weeks after the date of the test.

1. General information:

| 1.1 | Date of the test: | 21/01/04 |
| --- | --- | --- |
| 1.2 | Pre-selection, or Qualification ? (specify) | Pre-selection |
| 1.3 | Name of the ATLAS (or other) System: | TGC |
| 1.4 | Name of the board in the System: | HpT Board, SSW board, HSC board |
| 1.5 | Person responsible for the test: | Osamu Sasaki |
| 1.6 | Institute: | KEK |
| 1.7 | Email: | osamu.sasaki@kek.jp |
| 1.8 | Person responsible for RHA of the Board: | Osamu Sasaki |
| 1.9 | Institute: | KEK |
| 1.10 | Email: | osamu.sasaki@kek.jp |

2. Component:

| 2.1 | Name: | Gigabit Ethernet multimode transceiver |
| --- | --- | --- |
| 2.2 | Part Number: | V23818-K305-L57 |
| 2.3 | Type (see section 13.1): |  |
| 2.4 | Function (see section 13.1): | Optical/Electrical converter |
| 2.5 | Main specification of the component: Link from UXA15 to USA15 for the TGC muon level-1 trigger system. |
| 2.6 | Design (specify: COTS/ASIC): | COTS |
| 2.7 | Design center (if known): |  |
| Manufacturer: |  |
| 2.8 | Name of the manufacturer: | Infineon Technologies |
| 2.9 | Address of the manufacturer (if known): |  |
| 2.10 | Phone of the manufacturer (if known): |  |
| 2.11 | Email of the manufacturer (if known): |  |
| 2.12 | Web URL of the manufacturer (if known): | www.infineon.com |
| Sampling: |  |
| 2.13 | Number of tested components (irradiated): | 2 |
| 2.14 | Number of reference components (un-irradiated): | 1 |
| Batch origin: |  |
| 2.15 | Batch origin (Homogeneous/Unknown): |  |
| 2.16 | Manufacturing date code (for homogeneous batch): |  |
| 2.17 | Manufacturing line code (for homogeneous batch): |  |
| Technology: |  |
| 2.18 | Name of the technology (if known): |  |
| 2.19 | Technology (CMOS/BiCMOS/Bipolar/AsGa/Other): |  |
| 2.20 | Minimum geometry (m) : |  |
| Package: |  |
| 2.21 | Type: |  |
| 2.22 | Part number: |  |
| 2.23 | Number of pin: | 20 pins |
| 2.24 | Ceramic ? Plastic ? hybrid ? (specify) |  |

| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 2/6 Ref. DB: |
| --- | --- | --- |

3. Radiation:

| 3.1 | Name of the radiation facility: | Cyclotron and RI Center, Tohoku Univ. |
| --- | --- | --- |
| 3.2 | Address of the radiation facility: | Sendai, Japan |
| 3.3 | Radiation source (see 13.2) : | Cyclotron |
| 3.4 | Radiation type (see 13.2) : | Proton |
| 3.5 | Radiation energy (MeV) : | 70 MeV |
| 3.6 | Minimum & maximum flux (particle per second) : | 2.6 x 108 , 2.7 x 108 protons/sec/cm2 |
| 3.7 | Total fluence after last step (1 MeV eq. n/cm2) : | 5.4 x 1011 protons/cm2 |
| 3.8 | TID after last step (Gy) : | 870 Gy |
| 3.9 | Dosimetry / Calibration method: | -ray intensity of Cu foil |

4. Radiation test method (see 12.3):

| 4.1 | ATLAS Standard NIEL Test Method? | X |
| --- | --- | --- |
| 4.2 | Other TID test method (specify)? |

5. Thermal and voltage stresses:

| 5.1 | Temperature (oC) : | 24 - 35 OC |
| --- | --- | --- |
| 5.2 | Supply voltage (specify) : | 3.3 V |
| 5.3 | AC operation (Y/N) ? | Y |
| 5.4 | If “yes” to 5.3, which AC operation? Readout registers using the VME function. |
| 5.5 | If “yes” to 5.3, which frequency? |  |

Please select and complete one or several sections among sections 6 to 9, according to the device and function(s) you are testing:

6. If your circuit is an analog circuit or contains analog functions:

| 6.1 | Did you search for parasitic transient if any? | N |
| --- | --- | --- |
| 6.2 | Did you record parasitic transient if any? | N |
| 6.3 | Did you search for permanent dysfunction if any? | N |
| 6.4 | Did you record permanent dysfunction if any? | N |
| 6.5 | Did you measure current consumption? | Y |
| 6.6 | Did you record current consumption? | Y |
| 6.7 | Did you perform an automatic power cycle if a permanent dysfunction or current increase occurs? | N |
| 6.8 Description of operation and measurements of the analog (part of) circuit: |

| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 3/6 Ref. DB: |
| --- | --- | --- |

7. If your circuit is a digital circuit or contains digital functions:

| 7.1 | Did you check all functions in the circuit (Y/N) ? | Y |
| --- | --- | --- |
| 7.2 | If “no” to 6.13, which function did you not exercise (specify) ? |
| 7.3 | At what frequency did you exercise the circuit? | 800Mbps |
| 7.4 | Did you search for transient errors (Y/N) ? | Y |
| 7.5 | Did you automatically record transient errors if any (Y/N) ? | Y |
| 7.6 | Did you search for permanent errors (Y/N) ? | Y |
| 7.7 | Did you automatically record permanent errors if any (Y/N) ? | Y |
| 7.8 | Did you perform an automatic reset after a permanent error if any (Y/N) ? | N |
| 7.9 | Did you perform an automatic power cycle after a permanent error if any (Y/N) ? | N |
| 7.10 Description of operation and measurements of the digital (part of) circuit: Test Data are sent to an Rx chip and sent back to VME interface by a Tx chip. The data are compared with initial data. |

8. If your circuit is a memory or a register, or contains memory(ies) or registers:

| 8.1 | Did you check all the memories and registers of the device under test (Y/N) ? | Y |
| --- | --- | --- |
| 8.2 | If “no” to 8.1, which memories or registers will you not check (specify)? |
| 8.3 | Did you search for 0 => 1 upsets (Y/N) ? | Y |
| 8.4 | Did you search for 1 => 0 upsets (Y/N) ? | Y |
| 8.5 | Time required to write in the memory or in the register under test? |  |
| 8.6 | After a “write” sequence, do you read the memory or register once, or periodically (answer by “once” or “each [time between 2 consecutive read]”) ? | periodically |
| 8.7 | After a “write” sequence, what is the time during which the memory or the register is (once or periodically) read ? | periodically |
| 8.8 | Did you automatically record bit errors if any (Y/N) ? | Y |
| 8.9 | Did you check the “write” function of the memory or register after permanent upset if any (Y/N) ? | Y |
| 8.10 | Did you perform an automatic reset after permanent upset if any (Y/N) ? | N |
| 8.11 | Did you perform an automatic power cycle after permanent upset if any (Y/N) ? | N |
| 8.12 Description of operation and measurements of the memories and/or of the registers: User defined registers and read them/write test through the VME interface. |

| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 4/6 Ref. DB: |
| --- | --- | --- |

9. If your circuit is an elementary device:

| Power transistors |
| --- |
| 9.1 | Did you search for burnout ignition? |  |
| 9.2 | Did you record the rate of burnout ignition if any? |  |
| Optocouplers |
| 9.3 | Did you search for permanent dysfunction if any? |  |
| 9.4 | Did you record permanent dysfunction if any? |  |
| PIN diodes |
| 9.5 | Did you measure the rate of parasitic transient pulses (Y/N) ? |  |
| 9.6 | Did you record the rate of parasitic transient pulses? |  |
| 9.7 Description of operation and measurements of the device under test: |

10. Rejection criteria:

|  | Measured parameter | Rejection Criteria |
| --- | --- | --- |
| 10.1 |  |  |
| 10.2 |  |  |
| 10.3 |  |  |
| 10.4 |  |  |
| 10.5 |  |  |

11. Results:

|  | 11.1 | 11.2 | 11.3 | 11.4 | 11.4 | 11.5 | 11.6 | 11.7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Serial number of the device under test | number of SEU total fluence | number of bits permanently stuck total fluence | number of SEL total fluence | number of destructive SEE Total fluence | recovery after power cycle (Y/N)? | recovery after reset (Y/N)? | Failure mechanism (if any): for component “dead” or out of specification, give explanations and numbers |
| 1 | OE/EO 1 | 55 | 0 | 0 | 0 |  |  |  |
|  |  | 5.4E11 | 5.4E11 | 5.4E11 | 5.4E11 |  |  |  |
| 2 | OE/EO 2 | 14 | 0 | 0 | 0 |  |  |  |
|  |  | 2.7E11 | 2.7E11 | 2.7E11 | 2.7E11 |  |  |  |
| 3 |  |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |  |

| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 5/6 Ref. DB: |
| --- | --- | --- |

11. Results, cont.

|  | 11.1 | 11.2 | 11.3 | 11.4 | 11.4 | 11.5 | 11.6 | 11.7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Serial number of the device under test | number of SEU total fluence | number of bits permanently stuck total fluence | number of SEL total fluence | number of destructive SEE Total fluence | recovery after power cycle (Y/N)? | recovery after reset (Y/N)? | Failure mechanism (if any): for component “dead” or out of specification, give explanations and numbers |
| 6 |  |  |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |  |  |
| 13 |  |  |  |  |  |  |  |  |
| 14 |  |  |  |  |  |  |  |  |
| 15 |  |  |  |  |  |  |  |  |

12. Comments

Use the space below to comment test results, or to report them if the above-dedicated space is inappropriate for you.

| SEE | ATLAS STANDARD SEE TEST REPORT revision 3 (19-Jun-01) | Page 6/6 Ref. DB: |
| --- | --- | --- |

13. Guidelines

13.1 Type and Function

| Type | Function |
| --- | --- |
| Analogue device | ADC; Analogue memory; Analogue multiplexor; DAC; LVDS driver; LVDS receiver; Modulator/Demodulator; Voltage/Frequency converter |
| Data transmission Component | Receiver; Transceiver; Transmitter |
| Front-end electronic device | Drift Time Measurement; Multiple functions; Readout memory |
| Linear device | Amplifier; Comparator; Operational amplifier; Voltage reference; |
| Memory | SRAM |
| Microprocessor or peripheral | Microcontroller; Microprocessor |
| Optoelectronic component | Laser; Light emitting diode – LED; PIN diode; VCSEL |
| Power device | DC-DC converter; Power transistor; Voltage regulator |
| Programmable device | EEPROM; FPGA; Lookup table; Programmable delay |
| Passive component | Capacitor |
| Interfaces/Communication | LVDS; Switch |
| Mixed A/D device | Multiple functions |
| Logic gates | NOR, NAND, etc. |

13.2 Radiation source and type

| Source of radiation | Type of radiation |
| --- | --- |
| Accelerator | Electron, proton, spallation neutron |
| Am-241 | Ions (fission products) |
| Cf-252 | Ions (fission products) |
| Co-60 | Photon gamma 1.173 MeV and 1.332 MeV |
| Cs-137 | Photon gamma 0.662 MeV |
| Cyclotron | Proton, ion (specify), spallation neutron |
| Reactor | Neutron |
| Tandem accelerator | Protons, ions |
| Van-de-Graaf | Electron |
| X-Ray generator | Photon X |

13.3	Radiation test methods:

see ATLAS Policy on Radiation Tolerant Electronics rev. 2, pp. 20-26 http://atlas.web.cern.ch/Atlas/GROUPS/FRONTEND/WWW/RAD/RadWebPage/ATLASPolicy/APRTE_rev2_250800.pdf