Vc/11-Apr-04

### Week 15  starting 5April 04

### SM18 Operation Meeting (Tuesdays)

Bench status  and tests for now & next few days :

| Bench | Name | Status on Monday aft 5/04/04 | Temp |
| --- | --- | --- | --- |
| TBB1 | MBAR1051 | PT 5.2 1.5 KA Quench HF | 1.9 K |
| TBB2 | MBBL3122 | PT 13.2 Resist. Meas. | 300 K |
| TBC1 | MBAR2016 | PT 12 Warm Up | Warming |
| TBC2 | SSS0013 | SSS_Provoked Quench | 1.9 K |
| TBD1 | MBBL3118 | ICS 2 Connect Magnet (ICS) | 300 K |
| TBD2 | MBAL1062 | PT 5.1 1.5 KA Quench LF | 1.9 K |
| TBE1 | MBBL2081 | PT 10 Min. NRJ 11850 A | 1.9 K |
| TBE2 | MBBL3086 | Prep 5 Pumping + Cool Down | Cooling |
| TBF1 | MBAL1057 | Prep 2.2 IAP @ warm LF | 300 K |
| TBF2 | MBAL1061 | New Next 3111 ? | (no AntiC) |

EXPECTED NEW : 3119  ( no antic)

Test Coordinator this week: Marco B ; MTM support on call  :  (16-3602).

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Other General Issues

  - Easter Break & ICS work

  - Keep D1 free for SSS Mech Preparation ( 6 hrs ? )   J.Halik

[From 19 April…]

| Date | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- |
| Tuesday 30_N Wednesday 31_N | TBE1: HV insulation @warm connected to CFB. No communication between the server and the megger. TBD1: Same problem for HV cold. | AB-CO | HV | 2 mobiles rack were tried. Same problem. Federico called. He discovered that one switch in the RS 2323 C converter for the megger is in wrong position. Federico called and change switch position. Photo of the switch position pasted. The problem appeared again and the switch was moved to different position. |
| Wednesday 31_A Thursday 01_A | TBB: sun MTA42 does not allow sm 18 op account to access the storage of vol 8. | AB/CO | AQA | Quench analysis done with sun mta 33. Solved by Adrian. |
| Wednesday 31_N | TBB2 : Interlock “water” on PC | MTM |  | OK after closing other cluster’s valves. |
| Thursday 01_M | TBD1: For the SPA impossible to start the power: communication error. | MTM |  | Switch RS232 position error. Corrected by Federico. |
| Thursday 01_N | TBD2: IAP@warm Warning in the check of the sensor temperature TT821. | MTM | IAO | Check of the connection cables. But some warnings remain: NC open? |
| Friday 02_M Saturday_03_N | TBF1: Training quench: Message in TEMA. “Test type could not be defined”. PLCSE setting error. But the test is defined! Same problem on TBB2. | AB/CO | TEMA | Test aborted and re-launched then OK. |
| Friday 02_M Friday 02_N | TBB2: Acquisition problem. Differential signals saturated. Quench 5 where the four first cards signals were not present (D1-D2,…) Training quench 7: faults in AQA: signals are missing | MTM/AB CO??? | HF,LF | Federico called Adrian. Acquistion, cabling potaim-cards checked. Test re-launched and then OK for Q.6 Pierre will launch a deep investigation. |
| Friday 02_N | TBF1: HV test final at cold failed at MCS/ground. | MTM | HV | Rack changed. Then OK. |
| Saturday 03_M | TBD1: Still differences in readings between TT821(301 K) and Tcryo (184 K). | MTM/ACR |  | Is the correct probe read? TT 150 A to be read between 30 K and 300 K. TT148 between 30 K and 2 K. TT149 below 2 K. |
| Saturday 03_M | TBC1:IAP@cold. Launching test from TEMA no HF, LF graph were visible. They were running locally. | MTM | HF, LF | Applications closed and test re-launched. |
| Saturday 03_M | TBC1: The channel 2 of the Tektronix used for IAP is faulty. 6 V measured even without signals (Ram) | MTM |  | ???? |
| Saturday 03_M | TBB2: The access of the rotary switch is restricted by the presence of a pump. | ACR? |  | ACR team informed Monday . |
| Saturday 03_A | TBB2: Minimum energy. No charge of the power supply | MTM |  | Federico called. control crate of the power supplies is not conform. Exchange with cluster A the cable used to display the value of the charge has the wrong connector. |
| Saturday 03_A | TBE1: HV test problem with rack 1 : error while putting the megger in remote mode and megger getting switch off automatically during calibration. | MTM |  | Federico called. Internal problem in the battery of the megger. Message: Power down because battery is too low. Federico send an e-mail to Richard. Test performed with another rack. |
| Sunday 04_M | TBB2: Cryo team informs that there is an “ Anti cryostat fault” | ACR/MTM? |  | Federico informed and came. Fast decrease in temperature of TA1C1 from +20C to -12 C during 30 minutes. Then temp increased again and reached the good value. |
| Sunday 04_M | TBB2: Switch from B2 to CC: no lamp is glowing. | MTM |  | Federico informed. Many attempts. Ok after five times. |
| Sunday 04_A | TBB2: IAP@warm: Vtaps errors | MTM | IAP | Federico came. IAP re-launched. But problem remained. Giorgio forgot to restore two cables (link between potaim crates 1 and 3).Then OK (Jackie) |