Vc/21-Jun-04

### Week25  starting 14 June  04

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday 14 june ( ROCLA OK ?):

| Bench | Name | Situation Mon 14June pm |  | - |
| --- | --- | --- | --- | --- |
| TBA1 | MBAR3063 | Prep 5 Pumping + Cool Down | Q Antenna |  |
| TBA2 | MBBL3084 | waiting for Rocla 2015 next? | Shafts |  |
| TBB1 | MBBL1098 | Prep 5 Pumping + Cool Down |  |  |
| TBB2 | MBBL1120 | ICS 1 WP04 HV Test Warm |  |  |
| TBC1 | MBAL3140 | ICS 1 WP04 HV Test Warm |  |  |
| TBC2 | SSS 031 | PT 6.1 Training 1 |  |  |
| TBD1 | SSS11 | MM 2 LHC Cycle |  |  |
| TBD2 | _ | _ |  |  |
| TBE1 | MBBL1119 | PT 6.4 Training 4 |  |  |
| TBE2 | MBBL3067 | ICS 4 Final connection |  |  |
| TBF1 | MBBL1097 | ICS 2 Connect Magnet (ICS) | Shafts? |  |
| TBF2 | MBAL2059 | ICS 5 Traveller Last |  |  |

Test Coordinator this week: Stephane  ; MTM support on call :  (16-3602).

9 Magnets( 8 dipoles+ 1 SSS)   Disconnected after tests last week    ( Sat Midnight to Sat midnight)

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- D2  preparation mechanically for SSS

  - Repair Water leak in F cluster Power Converter ( 3 days asked) Mon to Wed

- SSS work :    AB-OP CERN Staff  daily(almost)  in new Rota

  - TO-DO List;  SSW & Surveyors Call out

Bench status  and tests for now( Monday 14/6 at 19.00)  & next few days :  see Video Display

| Magnets under Test on 14-06 6:48:47 PM |
| --- |
| - | Bench | Magnet | Shafts | Start | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | Last Test Desc | Time | I | Temp. | Total |
| 1 | TBA1 | MBAR3063 |  | 11-06 | 37 h. | 43 h. | - | - | - | PT 1 IAP @ cold | 14-06 (18 : 05) | 0 A. | 4.4 K | 80 hours |
| 2 | TBA2 | MBBL3084 |  | 07-06 | 22 h. | 53 h. | 44 h. | 14 h. | 29 h. | waiting for Rocla | 14-06 (13 : 49) | 0 A. | 300 K | 167 hours |
| 3 | TBB1 | MBBL1098 |  | 11-06 | 62 h. | 15 h. | - | - | - | Prep 5 Pumping + Cool Down | 14-06 (03 : 23) | 0 A. | Cooling | 77 hours |
| 4 | TBB2 | MBBL1120 |  | 14-06 | 51 h. | 99 h. | - | - | - | ICS 1 WP04 HV Test Warm | 14-06 (18 : 24) | 0 A. | 300 K | 150 hours |
| 5 | TBC1 | MBAL3140 |  | 14-06 | 3 h. | - | - | - | - | ICS 2 Connect Magnet (ICS) | 14-06 (18 : 39) | 0 A. | 300 K | 3 hours |
| 6 | TBC2 | SSS 031 |  | 10-06 | 64 h. | 22 h. | 19 h. | - | - | PT 6.1 Training 1 | 14-06 (15 : 40) | 12310 A. | 1.9 K | 105 hours |
| 7 | TBD1 | SSS11 |  | 27-05 | 180 h. | 86 h. | 176 h. | - | - | MM 2 LHC Cycle | 11-06 (19 : 07) | 0 A. | 1.9 K | 442 hours |
| 8 | TBE1 | MBBL1119 |  | 09-06 | 45 h. | 25 h. | 49 h. | - | - | PT 6.5 Training 5 | 14-06 (18 : 42) | 12200 A. | 1.9 K | 119 hours |
| 9 | TBE2 | MBBL3067 |  | 12-06 | 67 h. | - | - | - | - | ICS 4 Final connection | 14-06 (16 : 16) | 0 A. | 300 K | 67 hours |
| 10 | TBF1 | MBBL1097 |  | 14-06 | 16 h. | 974 h. | - | - | - | ICS 2 Connect Magnet (ICS) | 14-06 (15 : 40) | 0 A. | 300 K | 990 hours |
| 11 | TBF2 | MBAL2059 |  | 09-06 | 45 h. | 31 h. | 27 h. | 13 h. | 2 h. | ICS 5 Traveller Last | 14-06 (18 : 07) | 0 A. | 300 K | 118 hours |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| 1 | MBAR3063 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBBL3084 | 11230 Amp. (D2-L-S01) | 12440 Amp. (D1-L-S01) |  | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBL1098 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBL1120 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAL3140 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS 031 | 12310 Amp. (E_12) |  | - | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS11 | 11758 Amp. (No Data) | 12046 Amp. (I_12) | 12067 Amp. (I-34) | 12423 Amp. (E-12) | 12140 Amp. (E-34-S02) | 12568 Amp. (E 12-S06) | 12778 Amp. (E-34-S06) | 12856 Amp. () | - | - | - | - | - |
| 8 | MBBL1119 | 11350 Amp. (D2-U) | 11476 Amp. (D1_L) | 11821 Amp. (D1-L) | 12002 Amp. (D2-U) | 12200 Amp. (D1-L) |  | - | - | - | - | - | - | - |
| 9 | MBBL3067 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL1097 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 11 | MBAL2059 | 11638 Amp. (D2_L) | 11836 Amp. (D2_L) | 12006 Amp. (D2-L) | 12404 Amp. (D2-U) | 12749 Amp. (D2-l) | 12850 Amp. () | - | - | - | - | - | - | - |

# Results by Week

| Magnets under Test from 06-06-2004 to 12-06-2004 |
| --- |
| - | Bench | Magnet | Shafts | Start Date . | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA1 | MBBL3122 |  | 01-06-2004 | 51 h. | 45 h. | 32 h. | 17 h. | 16 h. | 11-06-2004 | 240 hours |  |  |
| 2 | TBA2 | MBAL3161 |  | 31-05-2004 | 59 h. | 30 h. | 32 h. | 18 h. | 28 h. | 07-06-2004 | 168 hours |  |  |
| 3 | TBB1 | MBAR2056 |  | 02-06-2004 | 41 h. | 34 h. | 25 h. | 15 h. | 30 h. | 11-06-2004 | 216 hours |  |  |
| 4 | TBB2 | MBBL1106 |  | 02-06-2004 | 18 h. | 23 h. | 21 h. | 17 h. | 42 h. | 08-06-2004 | 144 hours |  |  |
| 5 | TBC1 | MBBL2082 |  | 02-06-2004 | 33 h. | 27 h. | 28 h. | 19 h. | 5 h. | 08-06-2004 | 144 hours |  |  |
| 6 | TBC2 | SSS21 |  | 13-05-2004 | 14 h. | 82 h. | 391 h. | 7 h. | 112 h. | 07-06-2004 | 600 hours |  |  |
| 7 | TBE1 | MBAL3157 |  | 29-05-2004 | 74 h. | 44 h. | 51 h. | 27 h. | 46 h. | 09-06-2004 | 264 hours |  |  |
| 8 | TBE2 | MBAL1086 |  | 03-06-2004 | 45 h. | 41 h. | 50 h. | 15 h. | 16 h. | 11-06-2004 | 192 hours |  |  |
| 9 | TBF2 | MBBL1117 |  | 03-06-2004 | 46 h. | 32 h. | 22 h. | 15 h. | 17 h. | 09-06-2004 | 144 hours |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBL3122 | 12154 A. (D2_U) | 12398 A. (D2_U) | 12555 A. (D1-L) | 12692 A. (D1-U) | 12757 A. (D1-U) | 12798 A. (D1-L-S01) |  | - | - | - | - | - | - |
| 2 | MBAL3161 | 10694 A. (D1-U) | 12045 A. (D1-L) |  | - | - | - | - | - | - | - | - | - | - |
| 3 | MBAR2056 | 11723 A. (D2_L) | 12650 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBL1106 | 12101 A. (D1 L) | 12537 A. (D2-L) |  | - | - | - | - | - | - | - | - | - | - |
| 5 | MBBL2082 | 11641 A. (No Data) | 12265 A. (D1 U) |  | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS21 | 12003 A. (QE-34) | 12105 A. (QE-12) | 12458 A. (No Data) |  | - | - | - | - | - | - | - | - | - |
| 7 | MBAL3157 | 9662 A. (D1-U) | 10791 A. (No Data) | 12084 A. (D2_L) | 12570 A. (D2_U) | 12678 A. (D2 - U) | 12795 A. (D1_L) |  | - | - | - | - | - | - |
| 8 | MBAL1086 | 11122 A. (D2_U) | 11468 A. (D2-U) | 11818 A. (D1-U) | 12031 A. (D1_L) | 12338 A. (D1-L) | 12672 A. (D2-U) | 12772 A. (D1-L) | 12859 A. (D2-U) | 12850 A. | - | - | - | - |
| 9 | MBBL1117 | 11105 A. (D2_U) | 12050 A. (D2-L) |  | - | - | - | - | - | - | - | - | - | - |

- General Problems last week :

| Date | Bench | Problem | Type | Application/soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Thursday _10_A | TBA2 | Trigger on 2 potaim cards V_clamp_ext and V_supra_ext because Vtap lost during the cool down. | MTM |  | Ewald called. Following the advise of Giorgio a bridge on 7-8 cards on the double output was placed. |
| Thursday _10_N | TBA2 | The strap was not put in teh wrong pins. It triggers the potaim cards 5-6 . | MTM |  | A.Siemko corrected the position of the strap of the double output. Then OK. |
| Thursday _10_N | TBA2 | MM position : Wrong setting (3117 instead of 3084) | MTM | MMP | Ewald corrected the setting. |
| Thursday _10_N | TBB2 | Tcoil indicates low temperatures for few sectors. Values were correct in the Anti-cryostat display. | MTM |  |  |
| Friday _11_A | TBD1 | SSS11: SPA during LHC cycle. | MTM |  | Guy called and solved the problem. Quench and LHC cycle repeated. |
| Friday _11_A | TBC1 | During IAP at cold, compensation of AC signals difficult because of noise in some Voltages. | MTM | IAP | Guy and Richard managed to reduce the noise for signals less than 5 V, not for the other ones. |
| Saturday 12 _A | TBA2 | MM on 3081: Problem in rotation on shaft 24. RMS rotation speed >3%. | MTM |  | Stephane called. He checked the data and observed the rotation during the beginning of load-line. RMS degraded so he decided to stop the measurements. During the removal of the shaft the glue between the two ceramic sectors broke. |
| Saturday 12 _A | TBA1 | T of anticryostat not correct. The gamelle number not found. | MTM |  | GHH took the number in the box used for the connexion. |
| Saturday 12 _N | TBA1 | IAP at warm: T sensor gave wrong temperature 87 K instead of 300 K. | MTM |  | Stephane and Guy informed Sunday night. Stephane asked to check R sensor and the coefficient in MTF. |
| Saturday 12 _N | TBA1 | IAP at warm: Mag_300_X1 and Mag 300 air_X1 not OK. | MTM/ACR | IAP | Guy informed. Cryo problem. |
| Sunday 13 _M | TBE1 | Valve of water not working in automatic way. | MTM |  | Switch in manual mode. Valve moved by hand. |
| Sunday 13 _A | TBE1 | HF quench at 1.5 kA: Timing error. LF quench at 1.5 kA: QH not discharged. | MTM | hf, lf | Stephane called: He checked the signals. Give the OK to continue. The propagation of quench is too slow and pre-trigger time is not enough (3s). |
| Sunday 13 _N Monday_14_M | TBC2 | SSS HV test: Orbit dipole vs ground failed because the leads are freezing. IAP: AC compensation difficult to perform because AC source got loaded (4 volt cannot be maintained). | MTM MTM |  | Giorgio checked with the OP team the compensations. OK ON the scope the option -20 DB/decade was activated (too low gain)? |