Vc/14-Mar-05

### Week 11  starting 14  March 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  14 March 05 @ 3/14/2005 9:50:01 PM

| 8 | A1 | MBBL1184 | Prep 0 Scan Bench | 294.73 |
| --- | --- | --- | --- | --- |
| 6 | A2 | MBAR3258 | Prep 5 Pumping + Cool Down | 249.34 |
| 11 | B1 | SSS602 | ICS 2 Connect Magnet (ICS) | 292.4 |
| 10 | B2 | MBAR3251 | Prep 2.2 IAP @ warm HF | 293.57 |
| 5 | C1 | MBAR3256 | Prep 5 Pumping + Cool Down | 120.81 |
| 2 | C2 | MBAR3297 | PT 5.1 1.5 KA Quench LF | 4.20 |
| 3 | D1 | SSS036 | PT 2 HV Cold Test | 2.34 |
| 9 | D2 | SSS129 | PT 13.2 Resist. Meas. | 295.62 |
| 12 | E1 | MBBR3263 | Prep 0 Scan Bench | 294.64 |
| 4 | E2 | MBAR1046 | PT 2 HV Cold Test | 1.90 |
| 1 | F1 | MBAR3284 | Extra Provoked Quench | 1.90 |
| 7 | F2 | MBAR3303 | Prep 5 Pumping + Cool Down | 4.71 |

Coordinator this week: Marco; MTM support on call :   16-3602 .

14 Magnets Tested ( 2525 4th Time  included!! )

12  dipoles( 2 with MM)+ 2  SSS(1  with MM) +  0  SSSS

Disconnected after tests last week ( Sat Midnight to Sat midnight)

2143 Problem Magnet Last Saturday …on B2: All alerts Q_heaters Alarm. QH1 V min > 150; tmin V < 500; Tau Jump I > 6; E < 2000. QH YT 111: V min 297.2;tmin V 125;Tau Jump I 336; E 1903 . NO OK

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Situation on Repair :

General Points

SSSS

AOB

| Magnets under Test from 06-03-2005 to 12-03-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total |  |  |
| 1 | TBA1 | MBAL3144 |  |  | 04-03-2005 | 31 h. | 50 h. | 64 h. | 18 h. | 0 h. | 11-03-2005 | 163 h. |  |  |
| 2 | TBA2 | MBAL2129 |  |  | 03-03-2005 | 0 h. | 33 h. | 59 h. | 21 h. | 12 h. | 08-03-2005 | 125 h. |  |  |
| 3 | TBB2 | MBAL2156 |  |  | 02-03-2005 | 23 h. | 45 h. | 56 h. | 27 h. | 18 h. | 09-03-2005 | 169 h. |  |  |
| 4 | TBC1 | MBAL2149 |  |  | 04-03-2005 | 27 h. | 30 h. | 31 h. | 18 h. | 18 h. | 09-03-2005 | 124 h. |  |  |
| 5 | TBC2 | MBAL2150 |  |  | 01-03-2005 | 35 h. | 25 h. | 29 h. | 13 h. | 14 h. | 06-03-2005 | 116 h. |  |  |
| 6 | TBC2 | MBAL3150 |  |  | 06-03-2005 | 29 h. | 34 h. | 21 h. | 18 h. | 14 h. | 11-03-2005 | 116 h. |  |  |
| 7 | TBD1 | SSS106 |  |  | 05-03-2005 | 25 h. | 26 h. | 12 h. | 15 h. | 16 h. | 09-03-2005 | 94 h. |  |  |
| 8 | TBD2 | SSS019 |  |  | 02-03-2005 | 45 h. | 4 h. | 21 h. | 9 h. | 14 h. | 06-03-2005 | 93 h. |  |  |
| 9 | TBE1 | MBAR3287 |  |  | 04-03-2005 | 22 h. | 30 h. | 17 h. | 20 h. | 13 h. | 08-03-2005 | 102 h. |  |  |
| 10 | TBE2 | MBAR3296 |  |  | 08-03-2005 | 28 h. | 25 h. | 19 h. | 14 h. | 8 h. | 12-03-2005 | 94 h. |  |  |
| 11 | TBE2 | MBBL2137 |  |  | 03-03-2005 | 26 h. | 43 h. | 14 h. | 25 h. | 12 h. | 08-03-2005 | 120 h. |  |  |
| 12 | TBF1 | MBBR2525 |  |  | 06-03-2005 | 27 h. | 28 h. | 25 h. | 14 h. | 8 h. | 10-03-2005 | 102 h. |  |  |
| 13 | TBF2 | MBAL2154 |  |  | 03-03-2005 | 29 h. | 35 h. | 18 h. | 21 h. | 10 h. | 07-03-2005 | 113 h. |  |  |
| 14 | TBF2 | MBAR3249 |  |  | 07-03-2005 | 18 h. | 31 h. | 13 h. | 14 h. | 10 h. | 11-03-2005 | 86 h. |  |  |

### Quench Information 6 to 12 march 05

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL3144 | 8972 A. (D1-CFB) | 11480 A. (D2_L) | 11998 A. (D2-CF-S4) | 11790 A. (D2_U_CF) | 12015 A. (D2-MBS01) | 12250 A. (No Data) | 12578 A. (D2_L_CF) | 12741 A. (D2-U-CF3) | 12850 A. | - | - | - | - |
| 2 | MBAL2129 | 11235 A. (D2_U) | 12060 A. (D2-U) | 12219 A. (D2_L) | 12850 A. (D2-U-S02) | 12850 A. | - | - | - | - | - | - | - | - |
| 3 | MBAL2156 | 10839 A. (D1 _ U) | 12296 A. (D2_U) |  | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAL2149 | 10487.4 A. (D2-U) | 11710 A. (D2 - L) | 12468 A. (D1-U) | 12678 A. (D1-L) | 12798 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - |
| 5 | MBAL2150 | 11550 A. (D2-U) | 11432 A. (D2-U) | 12453 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 6 | MBAL3150 | 12190 A. (D2_U) | 12427 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS106 | 12197 A. (QI_34) | 12568 A. (QE-12) | 0 A. (No Data) |  | - | - | - | - | - | - | - | - | - |
| 8 | SSS019 | 11150 A. (QI_12) | 12200 A. (QI-34) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | MBAR3287 | 11473.8 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 10 | MBAR3296 | 12267 A. (D2_U) | 12240 A. (D2-U) | 12488 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |
| 11 | MBBL2137 | 11922 A. (D1_U) | 12856 A. | - | - | - | - | - | - | - | - | - | - | - |
| 12 | MBBR2525 | 12430.6 A. (D1_U_S01) | 12659 A. (D2-L-S02) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 13 | MBAL2154 | 11826 A. (D2_L) | 12833.9 A. (D1_U) |  | - | - | - | - | - | - | - | - | - | - |
| 14 | MBAR3249 | 12027 A. (D1-U) | 12765 A. (D1 - U) |  | - | - | - | - | - | - | - | - | - | - |

| From 06-03-2005 to 12-03-2005 |
| --- |
| - | Bench | Magnet Name | shafts | Start Date . | Connect Time | Wait +Cooling | Cold Tests | Wait +Warming | Disconnect Time | End Date . | Total | Q |
| 1 | TBF2 | MBAL2154 | False | 03-03-2005 | 29 h. | 35 h. | 18 h. | 21 h. | 10 h. | 07-03-2005 | 113 h. | 2 |
| 2 | TBF2 | MBAR3249 | False | 07-03-2005 | 18 h. | 31 h. | 13 h. | 14 h. | 10 h. | 11-03-2005 | 86 h. | 2 |
| 3 | TBF1 | MBBR2525 | True | 06-03-2005 | 27 h. | 28 h. | 25 h. | 14 h. | 8 h. | 10-03-2005 | 102 h. | 2 |
| 4 | TBE2 | MBAR3296 | False | 08-03-2005 | 28 h. | 25 h. | 19 h. | 14 h. | 8 h. | 12-03-2005 | 94 h. | 3 |
| 5 | TBE2 | MBBL2137 | False | 03-03-2005 | 26 h. | 43 h. | 14 h. | 25 h. | 12 h. | 08-03-2005 | 120 h. | 1 |
| 6 | TBE1 | MBAR3287 | False | 04-03-2005 | 22 h. | 30 h. | 17 h. | 20 h. | 13 h. | 08-03-2005 | 102 h. | 1 |
| 7 | TBD2 | SSS019 | False | 02-03-2005 | 45 h. | 4 h. | 21 h. | 9 h. | 14 h. | 06-03-2005 | 93 h. | 2 |
| 8 | TBD1 | SSS106 | False | 05-03-2005 | 25 h. | 26 h. | 12 h. | 15 h. | 16 h. | 09-03-2005 | 94 h. | 3 |
| 9 | TBC2 | MBAL2150 | False | 01-03-2005 | 35 h. | 25 h. | 29 h. | 13 h. | 14 h. | 06-03-2005 | 116 h. | 3 |
| 10 | TBC2 | MBAL3150 | False | 06-03-2005 | 29 h. | 34 h. | 21 h. | 18 h. | 14 h. | 11-03-2005 | 116 h. | 2 |
| 11 | TBC1 | MBAL2149 | False | 04-03-2005 | 27 h. | 30 h. | 31 h. | 18 h. | 18 h. | 09-03-2005 | 124 h. | 5 |
| 12 | TBB2 | MBAL2156 | False | 02-03-2005 | 23 h. | 45 h. | 56 h. | 27 h. | 18 h. | 09-03-2005 | 169 h. | 2 |
| 13 | TBA2 | MBAL2129 | True | 03-03-2005 | 0 h. | 33 h. | 59 h. | 21 h. | 12 h. | 08-03-2005 | 125 h. | 4 |
| 14 | TBA1 | MBAL3144 | True | 04-03-2005 | 31 h. | 50 h. | 64 h. | 18 h. | 0 h. | 11-03-2005 | 163 h. | 8 |

### Week 6 march05 to 13 March 05

### (   2156 long despite 2 quenches only because of   Cohabitation with SSSS on B1

### 3144 went into 2nd run so no disconnection   )

to end Feb 2005