Eric VERYUNES/16-May-05

### Week 19 starting 10 May. 05

### SM18 Operation Meeting (Tuesdays)

Bench status:

- Coordinator this week: V.Remondino;

- MTM support on call : G.D’Angelo .

- 18  Magnets Tested    :12  dipoles ( 2 with MM, MB1180, MB3293 ) + 6  SSS (1- Thermal cycle (SSS158))

- Situation From Cryogenics:  ACR Rep.

- Situation From Mechanics:

- SSS with anticryostat (SSS613,SSS156)

- wheel in the benches.

- silver shoe repair.

- AOB:

-SSS196 (Iearth).

-SSS155 (D1-D2 not compensated).

-Polarity switch on cluster B.

| Magnets under Test from 08-05-2005 to 14-05-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |  |
| 1 | TBA1 | MBAL1180 |  | 04-05-2005 | 28 h. | 29 h. | 48 h. | 17 h. | 20 h. | 10-05-2005 | 142 h. | Stripping |  |  |  |
| 2 | TBA1 | MBBL2167 |  | 10-05-2005 | 16 h. | 30 h. | 24 h. | 18 h. | 16 h. | 14-05-2005 | 104 h. | Stripping |  |  |  |
| 3 | TBA2 | MBBR3274 |  | 07-05-2005 | 33 h. | 22 h. | 16 h. | 14 h. | 7 h. | 10-05-2005 | 92 h. | Stripping |  |  |  |
| 4 | TBB1 | SSS131 |  | 04-05-2005 | 28 h. | 31 h. | 15 h. | 7 h. | 27 h. | 09-05-2005 | 108 h. | Stripping |  |  |  |
| 5 | TBB1 | SSS196(2) |  | 09-05-2005 | 34 h. | 15 h. | 32 h. | 7 h. | 2 h. | 13-05-2005 | 90 h. | Thermal cycle |  |  |  |
| 6 | TBB2 | SSS122 |  | 07-05-2005 | 36 h. | 14 h. | 30 h. | 11 h. | 17 h. | 12-05-2005 | 108 h. | Stripping |  |  |  |
| 7 | TBC1 | MBAR3325 |  | 01-05-2005 | 22 h. | 85 h. | 15 h. | 15 h. | 20 h. | 08-05-2005 | 157 h. | Stripping |  |  |  |
| 8 | TBC1 | MBBL1215 |  | 08-05-2005 | 25 h. | 22 h. | 21 h. | 15 h. | 13 h. | 12-05-2005 | 96 h. | Stripping |  |  |  |
| 9 | TBC2 | MBAL2073 |  | 06-05-2005 | 40 h. | 20 h. | 30 h. | 17 h. | 7 h. | 11-05-2005 | 114 h. | Stripping |  |  |  |
| 10 | TBD1 | SSS009(2) |  | 06-05-2005 | 41 h. | 7 h. | 28 h. | 11 h. | 13 h. | 10-05-2005 | 100 h. | Stand By |  |  |  |
| 11 | TBD2 | SSS158(2) |  | 06-05-2005 | 35 h. | 21 h. | 42 h. | 8 h. | 0 h. | 11-05-2005 | 106 h. | Thermal cycle |  |  |  |
| 12 | TBD2 | SSS158(2) |  | 11-05-2005 | 0 h. | 10 h. | 17 h. | 7 h. | 7 h. | 12-05-2005 | 41 h. | Stripping |  |  |  |
| 13 | TBE1 | MBAL3107 |  | 03-05-2005 | 34 h. | 26 h. | 16 h. | 14 h. | 20 h. | 08-05-2005 | 110 h. | Stripping |  |  |  |
| 14 | TBE1 | MBBR3265 |  | 08-05-2005 | 47 h. | 19 h. | 10 h. | 16 h. | 15 h. | 12-05-2005 | 107 h. | Stripping |  |  |  |
| 15 | TBE2 | MBAL2173(2) |  | 05-05-2005 | 0 h. | 24 h. | 9 h. | 13 h. | 23 h. | 09-05-2005 | 69 h. | Stripping |  |  |  |
| 16 | TBF1 | MBBR3268 |  | 09-05-2005 | 28 h. | 28 h. | 19 h. | 13 h. | 10 h. | 13-05-2005 | 98 h. | Stripping |  |  |  |
| 17 | TBF1 | MBBR3272 |  | 04-05-2005 | 34 h. | 31 h. | 18 h. | 14 h. | 19 h. | 09-05-2005 | 116 h. | Stripping |  |  |  |
| 18 | TBF2 | MBBR3293(3) |  | 06-05-2005 | 38 h. | 32 h. | 29 h. | 16 h. | 8 h. | 12-05-2005 | 123 h. | Stripping |  |  |  |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1180 | 12131 A. (D1-U-S13) | 12900 A. | - | - | - | - | - | - | - | - |
| 2 | MBBL2167 | 11080 A. (D2-U) | 11532 A. (D2-U) | 12309 A. (D2-U) | 12670 A. (D2-U) |  | - | - | - | - | - |
| 3 | MBBR3274 | 12728 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - | - |
| 4 | SSS131 | 12603 A. (QE_12) | 12830 A. (QE_34) | 12850 A. | - | - | - | - | - | - | - |
| 5 | SSS196 | 11918.3 A. (QI_34) | 12221 A. (QI_34) | 8385.3 A. (QI_34) | 12751.1 A. (QI_12) | 12850 A. | - | - | - | - | - |
| 6 | SSS122 | 12439 A. (QE_12) | 12711.6 A. (QE_12) | 12744.2 A. (QE-12) |  | - | - | - | - | - | - |
| 7 | MBAR3325 | 11325 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 8 | MBBL1215 | 11350 A. (D2_U) | 11918 A. (D1_U) | 12288 A. (D2_L) | 12360.4 A. (D2-L) |  | - | - | - | - | - |
| 9 | MBAL2073 | 11894 A. (D2-L) | 11857 A. (D1-L) | 12094 A. (D1_L) | 12238 A. (D1_L) | 12712.1 A. (D1-L) | 12850 A. | - | - | - | - |
| 10 | SSS009 |  | - | - | - | - | - | - | - | - | - |
| 11 | SSS158 | 11471.6 A. (QI-34) | 11617 A. (QE-12) | 12151 A. (QI-34) | 12377 A. (QI-12) | 12469 A. (QE-34) | 12556 A. (QE_12) | 12607.7 A. (QI_34) | 12685.6 A. (QE_12) | 12762 A. (QE-34) |  |
| 12 | SSS158 | 11763 A. (QI_34) | 12221.8 A. (QI-34) |  | - | - | - | - | - | - | - |
| 13 | MBAL3107 | 11763.6 A. (D2_L) | 12856 A. | - | - | - | - | - | - | - | - |
| 14 | MBBR3265 | 11967 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - |
| 15 | MBAL2173 | 12810 A. (D1-L) | 12900 A. | - | - | - | - | - | - | - | - |
| 16 | MBBR3268 | 12564 A. (D1_U) | 12785 A. (D1_L) |  | - | - | - | - | - | - | - |
| 17 | MBBR3272 | 12240.7 A. (D2-U) | 12848.5 A. (D2-U) | 12850 A. | - | - | - | - | - | - | - |
| 18 | MBBR3293 | 12422 A. (D2-L-S01) | 12706.4 A. (D2_U_S01) | 12850 A. | - | - | - | - | - | - | - |

### Week  08 May 05 to 14 May 05

Thermal Cycle

Light green: Connect + Pump down 	Blue :  Wait + Cool down

Ivory: Tests at Cold (36 hr)			Red :  Wait + Warm up (12 hr)	    Dark Green: Disconnect (8 hr)