### CHOHAN /15-August-05

### Week 33  starting 15 Aug 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  15 August 05 : 15/08/2005 15:28:12

| 9 | A1 | MBBL3138 | PT 13.1 IAP @ Warm | 301.89 |
| --- | --- | --- | --- | --- |
| 1 | A2 | MBAL1084 | HRR @ 1.8K - other | 1.88 |
| 4 | B1 | LE-C11R7 | Thermal cycle - No Tcoils | 5.12 HV |
| 12 | B2 | MBAL2190 | PT 13.2 Resist. Meas. | 297.68 |
| 10 | C1 |  |  | 295.8 |
| 2 | C2 | MBAL2182 | PT 12 Warm Up | 271.82 |
| 3 | D1 | SSS124 | PT 12 Warm Up | 10.41 |
| 11 | D2 | SSS607 | Magnet Alignment | 296.34 |
| 8 | E1 | MBAL3106 | ICS 4 Final connection | 298.04 |
| 6 | E2 | MBAL2208 | ICS 3 Traveller after warm test | 296.34 |
| 7 | F1 | MBBR2220 | ICS 2 Connect Magnet (ICS) | 295.8 |
| 5 | F2 | MBAR3348 | PT 2 HV Cold Test | 1.90 |

Tempr. from TBSM18 site

Coordinator this week: nick; MTM support 16-3602

14 complete Magnet Tests cycles

Only 10 dipoles ( 0 with MM )+ 1 SSS(without MM & SSW )

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight) Last week: Many Thermal cycles (Ansaldo) ; SSS607 (Q4) on D2 long tests; CC on B1 long cooling down…

- Situation From Cryogenics:  J-P Lamboy or ACR Rep.

- Leak on E1  Magnet this week (3106  )

Special  Points :

- Special SSS 607 on D2  (Roy +Marco)

- 1084  Lifetime tests : 200A/s cycles (Giorgio) + Instrumn.

- Connect. Cryostat Tests B1  (Lionel ?)

## Tests

| Magnets under Test from 07-08-2005 to 13-08-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAL2079 |  |  | 30-07-2005 | 37 h. | 23 h. | 46 h. | 17 h. | 42 h. | 07-08-2005 | 165 h. | Stripping |  |  |
| 2 | TBA1 | MBBL2194 |  |  | 07-08-2005 | 46 h. | 22 h. | 15 h. | 14 h. | 10 h. | 11-08-2005 | 107 h. | Stripping |  |  |
| 3 | TBA2 | MBBL1190 |  |  | 04-08-2005 | 38 h. | 21 h. | 18 h. | 14 h. | 28 h. | 09-08-2005 | 119 h. | Stripping |  |  |
| 4 | TBB2 | MBAL1241 |  |  | 03-08-2005 | 27 h. | 35 h. | 15 h. | 18 h. | 38 h. | 09-08-2005 | 133 h. | Stripping |  |  |
| 5 | TBC1 | MBAL2145 |  |  | 07-08-2005 | 35 h. | 11 h. | 17 h. | 19 h. | 16 h. | 11-08-2005 | 98 h. | Stripping |  |  |
| 6 | TBC2 | MBAL2182 |  |  | 08-08-2005 | 42 h. | 27 h. | 41 h. | - | - | 13-08-2005 | 110 h. | Not Found or Thermal cycle |  |  |
| 7 | TBC2 | MBAL2184 |  |  | 02-08-2005 | 45 h. | 20 h. | 17 h. | 13 h. | 26 h. | 08-08-2005 | 121 h. | Stripping |  |  |
| 8 | TBD1 | SSS206 |  |  | 02-08-2005 | 16 h. | 23 h. | 58 h. | 65 h. | 0 h. | 12-08-2005 | 162 h. | Not Found or Thermal cycle |  |  |
| 9 | TBD1 | SSS206 |  |  | 09-08-2005 | 0 h. | 17 h. | 20 h. | 9 h. | 26 h. | 12-08-2005 | 72 h. | Stand By |  |  |
| 10 | TBE1 | MBBL2187 |  |  | 05-08-2005 | 36 h. | 21 h. | - | - | - | 10-08-2005 | 105 h. | Not Found or Thermal cycle |  |  |
| 11 | TBE1 | MBBL2187 |  |  | 10-08-2005 | 0 h. | 21 h. | 12 h. | 20 h. | 23 h. | 13-08-2005 | 76 h. | Stripping |  |  |
| 12 | TBF1 | MBAL1248 |  |  | 05-08-2005 | 23 h. | 23 h. | 17 h. | 14 h. | 15 h. | 09-08-2005 | 92 h. | Stripping |  |  |
| 13 | TBF2 | MBBL2166 |  |  | 08-08-2005 | 35 h. | 21 h. | 15 h. | 16 h. | 8 h. | 12-08-2005 | 95 h. | Stripping |  |  |
| 14 | TBF2 | MBBR3387 |  |  | 02-08-2005 | 85 h. | - | - | - | - | 08-08-2005 | 128 h. | Stand By |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL2079 | 11970.3 A. (D2-L) | 12669.3 A. (D2-L) | 12787 A. (D1-L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBBL2194 | 11380 A. (D1_L) | 12311.1 A. (D2-L) | 12245 A. (D2_L) | 12444 A. (D1_U) |  | - | - | - | - | - | - | - | - |
| 3 | MBBL1190 | 12256.3 A. (D1_L) | 12849 A. (No Data) | 12851 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAL1241 | 12386.3 A. (D1-L) | 12849 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 5 | MBAL2145 | 11757 A. (D2_L) | 12672.1 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 6 | MBAL2182 | 10762 A. (D1-L) | 11231 A. (D1-L) | 11920 A. (D1_L) | 12206 A. (D1_L) | 12303 A. (D2_U) | 12444 A. (D1-U) | 12337 A. (D1_L) | 12397 A. (D1_U) | 12740 A. (D1_U) |  | - | - | - |
| 7 | MBAL2184 | 9920.7 A. (D1_L) | 11083.4 A. (D1_U) | 12266 A. (D1_U) | 12758.8 A. (D1_U) |  | - | - | - | - | - | - | - | - |
| 8 | SSS206 | 11323 A. (QE-34) | 11519 A. (QE-34) | 11845 A. (QE-34) | 12001 A. (QE_12) | 12415.5 A. (QE-34) | 12420 A. (QE-12) | 12585 A. (QI_12) | 12670 A. (QE-34) | 12795.4 A. (Q!-34) |  | - | - | - |
| 9 | SSS206 | 11858 A. (E_34) | 12405.9 A. (QE-34) |  | - | - | - | - | - | - | - | - | - | - |
| 10 | MBBL2187 | 11265 A. (D1-U) | 11692 A. (D2-U) | 12201 A. (D2-U) | 12373 A. (D2-U) | 12429.9 A. (D1-U) | 12488 A. (D1_U) | 12578.4 A. (D1_L) | 12653.9 A. (D1-L) | 12784.6 A. (D1-U) |  | - | - | - |
| 11 | MBBL2187 | 11924 A. (D1-U) | 12214.1 A. (D1_U) |  | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAL1248 | 12100 A. (D1_U) | 12387 A. (D2_L) | 12820 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 13 | MBBL2166 | 11927 A. (D1-U) | 12535 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 14 | MBBR3387 |  | - | - | - | - | - | - | - | - | - | - | - | - |

LEAK on 3387;   2187 had Thermal Cycle ;  sss206  had Thermal cycle ;    2182  had a Thermal cycle

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday _10_A | TBD1 | SSS206: Training quench 2, the signals QE, QI & Vtotal were completely flat. | AB/CO |  | Giorgio informed. He checked with lfoff and found that one acquisition card is to be replaced: done. |
| Wednesday _10_N | TBD1 | SSS206: PT10.1 (quench provoked at nominal) QH 1-2 discharged without any trigger generated and no QH 3-4 discharged. | MTM |  | QH re-charged. Warm_up quench performed. Meantime SPA occurred and no quench detected. |
| Thursday_11_N | TBD1 | SSS206: Resistance checks indicated the MO connection is crossed. No fault was found in the 904 | ICS |  | SSS put in stand-by. Error in cover flange. F.Gavin will correct it. |
| Friday_12_N | TBF1 | No communication between PLCSE and PLCHV. Problem on connector at cable side or HV Rack side | AB/CO-MTM |  | Solved temporarily holding up the cable. |
| Friday_12_N | TBD1 | Trigger in V_clamp E on SSS124 | ACR |  | Giorgio contacted. He advised to ask ICS to check the connection |
| Friday_12_N | TBA2 | Quench 4 on MB1084 : alarm that Vinit<810V for QH1(802V). | MTM |  | Check on QH graph: discharge OK. It was observed that the quench heater power supply was fluctuating between 802V and 810V. But that was quite stable after some time at 818 volts. Proceed with tests: QH OK for quench 5. |
| Saturday_13_M Saturday_13_A | TBB2 | MBAL2190 : AQA alert in PT5.2. | MTM |  | Giorgio contacted and he asked to repeat the test. Same alarm. Giorgio asked to perform : -to conduct resistance measurement -HV test (QH Investigation) Results: Dipole vs Quench Heater YT222 (525 V): Capacitance is not within expectation. (2) Quench Heater YT211 vs Ground (1850 V): Current higher than maximum specified value. (3) Quench Heater YT222 vs Ground (600 V & 1850 V): capacitance is not within expectation. Discharge checked by Giorgio: YT 211 is not working properly. |
| Saturday_13_A | TBA2 | MB1084: Magnet reached the ultimate at quench number 9. During the plateau at 12850 A, LF HF pressed to trigger the u file. Magnet quenched @ 12850 before LF could arm. | MTM |  | Magnet probably undergo to a thermal cycle after SSL @ 4.2 K. |
| Saturday_13_A | TBB2 | MB2190 : CDAP HV test failed on Dipole-QH vs Ground | MTM |  | TC and Giorgio decide d to warm up the magnet with quench at 3 kA with special protection (YT 211 replaced by YT212). |
| Sunday_14_A Sunday _14_N | TBA2 | Current cycling on MB1084 could not be continued because current lead temperature is 450 deg K. | ACR |  | Investigation by Cryogenic Team |
| Sunday_14_N | TBD1 | SSS124: could not power ‘EF circuit’ | MTM |  | Giorgio asked to continue with powering of GH and IJ circuits and with training quenches. |
| Sunday_14_N | TBD1 | SSS124: Magnet warm to 2.31 K suddenly | ACR |  | One communication card was changed by ACR team. |
| Monday 15_A | TBA1 | IAP at warm final on MB3138: Resistance measurements of the sextupole corrector show an open circuit. | ACR |  | Guy informed. |
| Monday 15_A | TBE1 | Leak on the MRB for MB3106 | ICS |  | Magnet has to be removed. |
| Monday 15_A | TBF1 | Communication failure between PLCHV and PLCSE. The problem is with the PLCSE cable. | AB/CO-MTM |  | Solved temporarily by tying the cable to higher point. |

# Text boxes

Green Connect + Pump down /Blue :  Wait + Cool down	Ivory: Tests at Cold (36 hr)Red :  Wait + Warm up (12 hr)	  Dark Green: Disconnect (8 hr)