| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday _23_N | TBB2 | MB3374: trigger during SPA at 1 kA. | MTM |  | Voltage level of the D1-D2 card still for SSS (100 mV). Voltage levels have to be better adjusted. |
| Wednesday_24_A | TBC2 | Insulation fault on cold initial before test connected to CFB temperature vs ground | MTM |  | Richard found the origin : humidity in the CFB current leads. |
| Wednesday_24_A | TBA2 | MB1084: CDAP failed at dipole -quench heaters Vs ground. | MTM |  | Richard found that the new installation for AC cables placed near the support of the main cables for the current leads are inducing a contact. Wires from the current leads to new connector were disconnected and test launched again |
| Wednesday _24_A | TBC2 | For MB3384 the manual MIITs for 1.5 kA quench heater discharges could not be registered. | AB/CO | AQA |  |
| Wednesday _24_N | TBA2 | MB1084: PTC10 - AQA alarm - DirVT voltage peak exceeded 200V. | MTM |  | Giorgio consulted. Check the curves and give the OK to continue |
| Thursday_25_N | TBE2 | No trigger for hf DAQ. | AB/CO | hf | Giorgio changed the CPU and the last DAQ cards. |
| Thursday_25_N | TBE2 | HWREC is not working. | ? | HWREC |  |
| Friday_26_A | TBD1 | SSS180 cooled down start. Anticryostat temperature went down. | MTM |  | P.Legrand checked and the resistances are working. Cold point coming from the magnet. Warm up the magnet. Disconnected and replaced. |
| Friday_26_A | TBF2 | trigger on potaim cards Vsum & Vtotal | MTM |  | Giorgio changed the potaim-card seven. |
| Saturday_27_M | TBC2 | ICS carried out WP04 instead of WP07. The original WP04 was overwritten by new file.. | ICS |  | The test name was changed in htm file and the file name was corrected in HV MTF Report folder. |
| Saturday_27_M | TBF2 | Power Supply for minimum energy (PT 10) is not working. No voltage reading. | MTM |  | Xavier forgot to restore the voltage readout cable in proper position. Giorgio fixed the problem. |
| Saturday_27_M | TBE1 | Leak suspected on MB3363. |  |  | Cryo team informed that quench can be performed only after their inspection/checking. |
| Sunday_28_M | TBA1 | MB2067: MinNRJ to warm up. Alarm Iearth>10 mA (12 mA). | MTM | AQA | Giorgio contacted. |
| Sunday_28_M | TBC2 | MB3388: HV test at warm: Dipole vs ground failed. | ICS |  | ICS will open the manchette and check the connections Bad connection found.. |
| Sunday_28_A | TBB2 | .ub file generated and SPA, no trigger recieved, Cryo OK lost | MTM/ACR? |  | ACR team said that a quench signal was received.. |
| Monday_29_M | All | MTF was not working. No connection to DB. | TS/CE |  |  |