### CHOHAN /26--sept 05

### Week 39 starting 26 Sept 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  26 Sept 05 : 9/26/2005 3:16:16 PM

| 10 | A1 | MBAL1221 | ICS 1 WP04 HV Test Warm | 296.88 |
| --- | --- | --- | --- | --- |
| 4 | A2 | MBBR1017 | PT 9 CDAP HV | 1.93 |
| 5 | B1 | SSS642 | PT 2 HV Cold Test | 1.90 |
| 2 | B2 | SSS215 | PT 6.2 Training 2 | 3.23 HV |
| 3 | C1 | MBAL3724 | PT 12 Warm Up | 225.42 |
| 9 | C2 | MBBR3385 | ICS 4 Final connection | 295.8 |
| 1 | D1 | SSS180 | MM 2 LHC Cycle | 1.90 |
| 12 | D2 |  |  | 295.89 |
| 8 | E1 | MBAR3394 | Prep 5 Cool Down | 296.25 |
| 6 | E2 | MBBL2203 | Prep 5 Cool Down | 92.05 |
| 11 | F1 | MBAR1252 | Prep 0 Scan Bench | 295.18 |
| 7 | F2 | MBBL2212 | Prep 5 Cool Down | 96.91 |

Tempr. from TBSM18 site

Coordinator this week: nikolay; MTM support Federico 16-3602

14 complete Magnet Tests cycles

Only 10 dipoles ( 0 with MM )+ 3 SSS(without MM & SSW )

+1 ssss (606 finally after 30 days on bench ) Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

- [  B1 WAS EMPTY FOR 5 Days ] ; hope D2 has not the same fate !

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Special  Points :

- Richard & Memo HV connector

- Special SSS on D2 : Q9  ( prospects & plans – J Halik )

- Power Supply tests for AB-PO (H Thiesen & Giorgio)

|  | AT/MTM |
| --- | --- |

Memo

To:	Operation team

From:	Richard Mompo, Patrick Legrand, Frederic Flamand

Date:	21 Septembre 2005

- New connection on top of CFBs

Frederic Flamand has prepared an installation to ease the connection and disconnection of the cables needed for warm and AC measurements and also to avoid touching the current leads that can be very hot.

We discovered later on that those cables were causing problems during HV tests at 3100Volts.

So the electrical insulation of the cables was reinforced, on all 6 clusters, in order to carry out HV tests without having to disconnect those cables anymore! The cables (with brown sleeves cf. picture), between the current leads and the aluminum holds, can remain connected during the whole run of a magnet.

| Magnets under Test from 18-09-2005 to 24-09-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAL3399 |  |  | 14-09-2005 | 30 h. | 23 h. | 19 h. | 26 h. | 11 h. | 19-09-2005 | 109 h. | Stripping |  |  |
| 2 | TBB2 | SSS284 |  |  | 20-09-2005 | 32 h. | 14 h. | 14 h. | 7 h. | 16 h. | 23-09-2005 | 83 h. | Stripping |  |  |
| 3 | TBB2 | SSS343 |  |  | 16-09-2005 | 32 h. | 16 h. | 14 h. | 7 h. | 15 h. | 19-09-2005 | 84 h. | Stripping |  |  |
| 4 | TBC1 | MBAR2227 |  |  | 19-09-2005 | 19 h. | 26 h. | 18 h. | 12 h. | 12 h. | 23-09-2005 | 87 h. | Stripping |  |  |
| 5 | TBC1 | MBBL2214 |  |  | 14-09-2005 | 33 h. | 19 h. | 38 h. | 23 h. | 15 h. | 19-09-2005 | 128 h. | Stripping |  |  |
| 6 | TBC2 | MBAR2230 |  |  | 16-09-2005 | 37 h. | 32 h. | 15 h. | 15 h. | 15 h. | 21-09-2005 | 114 h. | Stripping |  |  |
| 7 | TBD1 | SSS293 |  |  | 10-09-2005 | 68 h. | 74 h. | 22 h. | 13 h. | 11 h. | 18-09-2005 | 188 h. | Stripping |  |  |
| 8 | TBD2 | SSS606 |  |  | 08-09-2005 | 0 h. | 19 h. | 269 h. | 18 h. | 49 h. | 23-09-2005 | 355 h. | Stand By |  |  |
| 9 | TBE1 | MBAL1201 |  |  | 17-09-2005 | 28 h. | 31 h. | 13 h. | 13 h. | 7 h. | 20-09-2005 | 92 h. | Stripping |  |  |
| 10 | TBE2 | MBBL2201 |  |  | 18-09-2005 | 38 h. | 26 h. | 22 h. | 32 h. | 11 h. | 24-09-2005 | 129 h. | Stripping |  |  |
| 11 | TBE2 | MBBL2217 |  |  | 13-09-2005 | 31 h. | 24 h. | 37 h. | 16 h. | 11 h. | 18-09-2005 | 119 h. | Stripping |  |  |
| 12 | TBF1 | MBAL1250 |  |  | 17-09-2005 | 32 h. | 22 h. | 14 h. | 18 h. | 19 h. | 22-09-2005 | 105 h. | Stripping |  |  |
| 13 | TBF2 | MBAL2134 |  |  | 20-09-2005 | 22 h. | 23 h. | 14 h. | 14 h. | 15 h. | 24-09-2005 | 88 h. | Stripping |  |  |
| 14 | TBF2 | MBAL3401 |  |  | 16-09-2005 | 28 h. | 24 h. | 17 h. | 14 h. | 10 h. | 20-09-2005 | 93 h. | Stripping |  |  |

### Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL3399 | 9636 A. (D1_U) | 11758 A. (D1_U) | 12583 A. (D1_U) | 12845 A. (D1_L) |  | - | - | - | - | - | - | - | - |
| 2 | SSS284 | 12552 A. (QE-34) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 3 | SSS343 | 12567 A. (QI-34) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 4 | MBAR2227 | 11350 A. (D1-L) | 12197 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 5 | MBBL2214 | 10147 A. (D2_U) | 11996 A. (D1_L) | 12839 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 6 | MBAR2230 | 11565.4 A. (D1_L) | 12150.3 A. (D1_U) | 12462.2 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |
| 7 | SSS293 | 11410 A. (QI-34) | 11869 A. (QE-12) | 12278 A. (QI_12) | 12514.8 A. (QE_12) |  | - | - | - | - | - | - | - | - |
| 8 | SSS606 | 3968 A. (MQM-E-2) | 4137 A. (MQM_E_2) | 4224 A. (MQM_I_2) | 4248 A. (MQM-I-2) | 4286 A. (MQM-I-1) | 4310 A. (MQM-E-1) | 4324 A. (MQM-I-1) | 4324.4 A. (MQM-E-1) | 4351 A. (MQM- I-1) | 4381 A. (MQM-E-2) | 4403 A. (MQM_I_2) | 4400 A. (MQM-E-1) | 4429.8 A. (MQM_E_2) |  |
| 9 | MBAL1201 | 12643 A. (D2_L) | 12856 A. | - | - | - | - | - | - | - | - | - | - | - |  |
| 10 | MBBL2201 | 11623 A. (D1_U) | 12568 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |  |
| 11 | MBBL2217 | 11186 A. (D1-U) | 12513 A. (D2-L) | 12857 A. | - | - | - | - | - | - | - | - | - | - |  |
| 12 | MBAL1250 | 12473 A. (D1_L) | 12630 A. (D2_U) | 12840 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |  |
| 13 | MBAL2134 | 10857 A. (D2-L) | 12657 A. (D1_L) | 12848 A. (D2-U) |  | - | - | - | - | - | - | - | - | - |  |
| 14 | MBAL3401 | 12290 A. (D1_L) | 12391 A. (D2_L) | 12864 A. (D2_U) |  | - | - | - | - | - | - | - | - | - |  |

Shows Cohabitation D1 – D2 really is a problem !!  SSS on D2 only needed 3 quenches.  D2 is waiting and at cold while D1 is being worked on.

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Thursday_22_M | TBD1 | Resistance &voltage measurements at warm after cold test: The sextupole voltage taps have incorrect measurement values. | MTM |  | TC informed. NC opened. On TC's advise the magnet has been signed for stripping as the sextupoles have been trained to the ultimate value of 600A |
| Thursday_22_N | TBC1 | IAP after cold tests on MB2227: signals are not as expected while the same file analysed with hfoff shows correct results | MTM | IAP | Giorgio called. He asked to proceed with the program and will investigate the problem tomorrow. |
| Friday_23_N | TBE | Cycles on MB1017 aborted due to cryo-loss. | ACR |  |  |
| Saturday_24_M | TBB2 | Oracle error on TT821 in HWREC when launching IAP at warm. HWREC, files are missing. | CRI |  | Giorgio called. The thermometer was changed for this magnet. The coefficients were present in MTF but not loaded by HWREC. He put the HWREC off and created the settings accordingly. |
| Saturday_24_M | TBB2 | Quench heaters did not discharge when power supply were on. | MTM |  | Giorgio came. The security matrix was configured for a special SSS. The connector place needed to be changed. |
| Saturday_24_M | TBD1 | Not-correct results SSW measurements on SSS180. | MTM |  | Guy called. He came and found that the system is not responding correctly because after switched off once one config script has to be re-launched. |
| Saturday_24_M | TBA1 | Diode test could not be launched. Power supply for LF heater did not charged fully. | MTM |  | Giorgio came and solved the problem by changing the capacitor bank. |
| Sunday_25_A | TBD1 | MM1 SSS180. Hardware and configuration fle problem. | MTM |  | Giorgio explained the procedure for launching MM1. He also came in SM18 because one shaft connector was not correctly plugged. He also uploaded the new coil factor in the DB. |
| Sunday_25_N | TBB2 | On SSS 215 provoked quench 1/2 HF did not show the complete results because of an analysis error: as the configuration file was not generated correctly. | MTM |  | Giorgio advised to proceed further .He completed the config. file Monday morning. |
| Monday_26_A | TBD1 | MM4 (magnetic measurements on corrector) could not be launched. It was not possible to change the power supply from CD to EF | MTM |  | The ramp was on 20 A/s in place of 2 A/s |

# Text boxes

DC cable   and   AC cable

Permanent connection