### Chohan /31-Oct-05

### Week 44 starting 31Oct 05

### SM18 Operation Meeting (Tuesdays)

Bench status  on Monday  24Oct 05 :  10/31/2005 10:20:08 AM

| 1 | A1 | MBBL3409 | ICS 5 Traveller Last | 295.18 |
| --- | --- | --- | --- | --- |
| 9 | A2 | MBBR3340 | Prep 5 Cool Down | 171.95 |
| 10 | B1 | SSS653 | Prep 1 Lyre Test | 294.64 |
| 5 | B2 | SSS166 | Prep 0 Scan Bench | 295.8 |
| 11 | C1 | MBBL3407 | Prep 2.1 IAP @ warm LF | 293.57 |
| 6 | C2 | MBBR3415 | ICS 5 Traveller Last | 295.8 |
| 4 | D1 | SSS272 | PT 9 CDAP HV | 1.89 |
| 3 | D2 | SSS631 | Prep 5 Cool Down | 1.90 |
| 7 | E1 | MBAR1270 | Prep 5 Cool Down | 21.85 |
| 2 | E2 | MBAL1072 | PT 12 Warm Up | 272.35 |
| 12 | F1 | MBAR1264 | ICS 4 Final connection | 294.1 |
| 8 | F2 | MBAL3395 | PT 13.2 Resist. Meas. | 296.88 |

Tempr. from TBSM18 site

Coordinator this week: Vittorio; MTM support: 16-3602

Only 15 complete Magnet Tests cycles  from 11 benches ( E2 was still under CFB repair)   10 Dipoles + 3  SSS  + 2 SSSS

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

E2 CFB (leak) is now Repaired, 4 weeks down time 29-sept-05 till 27-oct-05.

Special  Points :

- Connection Problems for Sp SSS on B1 (ICS + )

- 3139 re-test and signals

- Special SSS631  on D2 :   SSW & Chaconsa ? (pgm Marco)

- SSW   problems on dipole 3409  &  MM cancelled( Marco+Stephane).

AOB

| Magnets under Test from 23-10-2005 to 29-10-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |  |
| 1 | TBA1 | MBAR1275 |  | 21-10-2005 | 33 h. | 27 h. | 23 h. | 15 h. | 17 h. | 26-10-2005 | 115 h. | Stripping |  |  |  |
| 2 | TBA2 | MBAL1154 |  | 19-10-2005 | 28 h. | 44 h. | 27 h. | 16 h. | 14 h. | 24-10-2005 | 129 h. | Stripping |  |  |  |
| 3 | TBA2 | MBBL3408 |  | 24-10-2005 | 25 h. | 23 h. | 44 h. | 19 h. | 7 h. | 29-10-2005 | 118 h. | Stripping |  |  |  |
| 4 | TBB1 | SSS638 |  | 20-10-2005 | 31 h. | 28 h. | 77 h. | 19 h. | 25 h. | 28-10-2005 | 180 h. | Stripping |  |  |  |
| 5 | TBB2 | SSS150 |  | 20-10-2005 | 29 h. | 19 h. | 19 h. | 9 h. | 13 h. | 23-10-2005 | 89 h. | Stripping |  |  |  |
| 6 | TBB2 | SSS162 |  | 23-10-2005 | 33 h. | 17 h. | 22 h. | 7 h. | 10 h. | 27-10-2005 | 89 h. | Stripping |  |  |  |
| 7 | TBC1 | MBAL2192(2) |  | 21-10-2005 | 0 h. | 20 h. | 9 h. | 15 h. | 20 h. | 24-10-2005 | 64 h. | Stripping |  |  |  |
| 8 | TBC2 | MBBL3405 |  | 22-10-2005 | 28 h. | 22 h. | 19 h. | 12 h. | 13 h. | 26-10-2005 | 94 h. | Stripping |  |  |  |
| 9 | TBD1 | SSS292(2) |  | 22-10-2005 | 0 h. | 21 h. | 91 h. | 8 h. | 20 h. | 28-10-2005 | 140 h. | Stripping |  |  |  |
| 10 | TBD2 | SSS604 |  | 11-10-2005 | 63 h. | 23 h. | 175 h. | 72 h. | 18 h. | 25-10-2005 | 351 h. | Stand By |  |  |  |
| 11 | TBE1 | MBAL3708 |  | 25-10-2005 | 27 h. | 19 h. | 21 h. | 14 h. | 12 h. | 29-10-2005 | 93 h. | Stripping |  |  |  |
| 12 | TBE1 | MBBL3404 |  | 19-10-2005 | 27 h. | 47 h. | 22 h. | 15 h. | 21 h. | 25-10-2005 | 132 h. | Stripping |  |  |  |
| 13 | TBF1 | MBAR2236 |  | 20-10-2005 | 24 h. | 46 h. | 5 h. | 19 h. | 24 h. | 25-10-2005 | 118 h. | Stand By |  |  |  |
| 14 | TBF2 | MBAL2198 |  | 18-10-2005 | 27 h. | 25 h. | 21 h. | 15 h. | 8 h. | 23-10-2005 | 96 h. | Stripping |  |  |  |
| 15 | TBF2 | MBAL2210 |  | 23-10-2005 | 31 h. | 26 h. | 16 h. | 13 h. | 19 h. | 27-10-2005 | 105 h. | Stripping |  |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAR1275 | 12204.3 A. (D1-L-S01) | 12596.3 A. (D1_U_S06) |  | - | - | - | - | - | - | - |
| 2 | MBAL1154 | 12432 A. (D2_L) | 12696.5 A. (D2_L) | 12726.3 A. (D1-L) |  | - | - | - | - | - | - |
| 3 | MBBL3408 | 12049.3 A. (D2_U) | 12759.5 A. (D1_L) | 12536.9 A. (D1_L) |  | - | - | - | - | - | - |
| 4 | SSS638 | 5017.2 A. (MQML-E12) | 5601.3 A. (MQML_I34) | 5820 A. | - | - | - | - | - | - | - |
| 5 | SSS150 | 12545.9 A. (QI-12) | 12639.3 A. (QI-34) | 12800 A. | - | - | - | - | - | - | - |
| 6 | SSS162 | 12514 A. (QI-34) | 12843 A. | - | - | - | - | - | - | - | - |
| 7 | MBAL2192 | 11907.8 A. (D2_U) | 12773 A. (D2 - U) |  | - | - | - | - | - | - | - |
| 8 | MBBL3405 | 1234.2 A. (D2_U) | 12274.3 A. (D1_L) | 12792.4 A. (D2-L) |  | - | - | - | - | - | - |
| 9 | SSS292 | 11496.3 A. (QE_34) | 12183.9 A. (QI-12-S5) | 12527.4 A. (QI-34-S6) |  | - | - | - | - | - | - |
| 10 | SSS604 | 5409.7 A. (MQM1-Ext) | 5820 A. | - | - | - | - | - | - | - | - |
| 11 | MBAL3708 | 12396.7 A. (D2_L) | 12387.1 A. (D1-U) | 12857 A. | - | - | - | - | - | - | - |
| 12 | MBBL3404 | 9498.7 A. (D2-U) | 11871.7 A. (D2-U) | 12203.1 A. (D2-U) | 12627.1 A. (D2-U) | 12639.3 A. (D2_L) | 12832.5 A. (D2-L) | 12850 A. | 12857 A. | - | - | - |
| 13 | MBAR2236 |  | - | - | - | - | - | - | - | - | - |  |
| 14 | MBAL2198 | 10081.3 A. (D1_U) | 11110.4 A. (D2_L) | 12129.6 A. (D1_L) | 12676.4 A. (D2_L) | 12850 A. | - | - | - | - | - |  |
| 15 | MBAL2210 | 10804.1 A. (D1-U) | 12421.7 A. (D1-L) | 12389.3 A. (D1_L) |  | - | - | - | - | - | - |  |

COHABITATION Issues  on B & D clusters as usual  due to Special SSS 604 (D2, Chaconsa , etc)    &  638( on B1 )

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_25_A | TBD1 | EF corrector test at 600 A (MQT). Power supply deliver error message” digital parameters out of limits”. | AB/PO |  | Richard came and tried many times. At the end the measurements were launched. Investigation by AB/PO Friday. Inductance loop not correct. |
| Wednesday_26_M | TBB2 | Corrector powering on SSS162 could not be started as the PC Aux interlock in PLCSE is not clearing. | AB/PO |  | 120A power supply stop button was found in the "OFF" position |
| Thursday_27_A | TBD1 | TT821 on MB3139 is not working at cold (already reported during the first run). | AB/PO |  | NC opened. Richard measured the probe at the level of the IFS box. One contact is open. |
| Thursday_27_A | TBD1 | IAP @warm final on SSS292: The results on aperture voltages displayed were not correct. | AB/CO | IAP | OP team checked the results with lf DAQ. |
| Thursday_27_M | TBA2 | Angle measurements on MB3408: SSW3 did not work. | MTM |  | Nikolay advised to change with system 1. Measurements during Thursday night; wire broke 4 times. Stephane and Marco decided to restrict the number of measurements. |
| Friday_28_A | TBA1 | MB1072: From VT measurements no diode in the magnet. | MTM |  | NC opned. MB1072 is in the list of diode work from D.Tommasini. It will not influence the decision stripping/stand by. |
| Friday_28_A | TBF1 | MB2209: While launching PT5.1 a message appeared on the local server” One or more channels have < 100 ms pre-trigger time”. You have to acknowledge to arm hf and lf DAQ. | AB/CO | Hf,lf | Not blocking. Configuration corrected by Richard. Problem known for all benches. Richard asked Maryline for a correction asp. |
| Friday_28_N | TBD1 | SSS272: Permanent trigger in VclampD and VclampF. Voltage measured VclampD=10V VclampF=-6.5V | ICS |  | ICS is asked to check the connection |
| Saturday_29_M | TBA1 | Leak found in MB3409. | ACR |  | Investigation by cryo team: Leak in the flexible of the line E. Decision was to continue the test. MB3409 leak test could not be validated. It has to be reconnected and leak test redone. |
| Saturday_29_M | TBB1 | ICS cannot connect SSS653 because of a piece to be inserted in the cover line block has not the proper thickness. | ICS |  | B.Poulnais gave to ICS team the correct piece. |
| Sunday_30_M | TBC1 | Corrector magnets were found open during the final resistance measurement CDW2 for the MB3139. | MTM |  | NC opened. Stephane’s comment : Magnet already stripped after the first run: correctors not connected. |
| Sunday_30_N | TBD1 | RMD did not work: “PC fault” displayed. | AB/PO |  | Richard came and reset the Digital Controler. |
| Sunday_30_N | TBB2 | SSS166: Bar code not correct. |  |  | NC opened. |