### Chohan /07-Nov-05

### Week 45 starting 07 Nov 05

### SM18 Operation Meeting (Tuesdays)

Bench status on Monday 07 Nov 05:  11/7/2005 10:14:11 AM

| 7 | A1 | MBBR3390 | Prep 5 Cool Down | 120.23 |
| --- | --- | --- | --- | --- |
| 1 | A2 | MBAL3412 | PT 12 Warm Up | 240.99 |
| 2 | B1 | SSS261 | PT 12 Warm Up | 301.35 |
| 5 | B2 | SSS033 | PT 6.2 Training 2 | 9.19 |
| 4 | C1 | MBBL3653 | PT 5.1 1.5 KA Quench LF | 1.91 |
| 8 | C2 | MBBR2241 | ICS 1 WP04 HV Test Warm | 294.1 |
| 11 | D1 | SSS218 | PT 14 Magnet MAPS | 292.4 |
| 3 | D2 | SSS631 | SCAN 3 | 1.91 |
| 12 | E1 | MBAR1273 | PT 14 Magnet MAPS | 294.1 |
| 9 | E2 | MBAR1255 | PT 14 Magnet MAPS | 296.88 |
| 6 | F1 | MBAR2248 | PT 8 Fast De-excitation | 1.90 |
| 10 | F2 |  |  | 292.4 |

Tempr. from TBSM18 site

Coordinator this week: Pierre; MTM support: 16-3602

Only 15 complete Magnet Tests cycles from 12 benches 11 Dipoles (3409 Leak) + 3 SSS + 1 SSSS

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Special Points:

- Sunday 6/11 midday    Rocla : Not possible to change anymore magnets !

- SSSS631:  Was on ready for Chaconsa last  Fri lunchtime but no one to do it ( Marco ?) ; How much more  time for MM this week?

AOB

| Magnets under Test from 30-10-2005 to 05-11-2005 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBBL3409(2) |  | 26-10-2005 | 32 h. | 20 h. | 21 h. | 16 h. | 14 h. | 01-11-2005 | 103 h. | Stand By |
| 2 | TBA1 | MBBL3409(2) |  | 01-11-2005 | 16 h. | 22 h. | 9 h. | 21 h. | 12 h. | 05-11-2005 | 80 h. | Stripping |
| 3 | TBA2 | MBBR3340 |  | 29-10-2005 | 32 h. | 24 h. | 43 h. | 16 h. | 14 h. | 04-11-2005 | 129 h. | Stripping |
| 4 | TBB1 | SSS653 |  | 28-10-2005 | 87 h. | 14 h. | 25 h. | 17 h. | 25 h. | 04-11-2005 | 168 h. | Stand By |
| 5 | TBB2 | SSS113 |  | 27-10-2005 | 28 h. | 13 h. | 17 h. | 8 h. | 9 h. | 30-10-2005 | 75 h. | Stripping |
| 6 | TBB2 | SSS166 |  | 30-10-2005 | 35 h. | 12 h. | 37 h. | 17 h. | 14 h. | 04-11-2005 | 115 h. | Stripping |
| 7 | TBC1 | MBAL3139(2) |  | 24-10-2005 | 27 h. | 21 h. | 25 h. | 61 h. | 18 h. | 30-10-2005 | 152 h. | Stripping |
| 8 | TBC1 | MBBL3407 |  | 30-10-2005 | 35 h. | 32 h. | 16 h. | 15 h. | 13 h. | 04-11-2005 | 111 h. | Stripping |
| 9 | TBC2 | MBBR3415 |  | 26-10-2005 | 39 h. | 25 h. | 17 h. | 15 h. | 17 h. | 31-10-2005 | 113 h. | Stripping |
| 10 | TBD1 | SSS272 |  | 28-10-2005 | 40 h. | 11 h. | 16 h. | 9 h. | 15 h. | 01-11-2005 | 91 h. | Stripping |
| 11 | TBE1 | MBAR1270 |  | 29-10-2005 | 23 h. | 22 h. | 14 h. | 12 h. | 21 h. | 02-11-2005 | 92 h. | Stripping |
| 12 | TBE2 | MBAL1072 |  | 27-10-2005 | 36 h. | 21 h. | 13 h. | 17 h. | 24 h. | 01-11-2005 | 111 h. | Stripping |
| 13 | TBF1 | MBAL2209 |  | 25-10-2005 | 39 h. | 25 h. | 18 h. | 15 h. | 13 h. | 30-10-2005 | 110 h. | Stripping |
| 14 | TBF1 | MBAR1264 |  | 30-10-2005 | 35 h. | 26 h. | 23 h. | 20 h. | 16 h. | 04-11-2005 | 120 h. | Stripping |
| 15 | TBF2 | MBAL3395 |  | 27-10-2005 | 22 h. | 35 h. | 10 h. | 15 h. | 35 h. | 01-11-2005 | 117 h. | Stripping |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| 1 | MBBL3409 | 12995.2 A. (D1-U) | 12840.4 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - |
| 2 | MBBL3409 | 11524.4 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - | - |
| 3 | MBBR3340 | 10336.4 A. (D2_L) | 12068.5 A. (D2_L) | 12390.6 A. (D1-U-S01) | 12684.2 A. (D2_U_S13) | 12850 A. | - | - | - | - | - |
| 4 | SSS653 | 5434 A. (MQM_E) | 5674 A. (MQM_E) | 5820 A. | - | - | - | - | - | - | - |
| 5 | SSS113 | 10379.8 A. (QE_12) | 12358.3 A. (QE_12) | 12657.3 A. (QE_34) |  | - | - | - | - | - | - |
| 6 | SSS166 | 11672.1 A. (QE-12) | 12340.8 A. (QI-34) | 12729.1 A. (QI_34) |  | - | - | - | - | - | - |
| 7 | MBAL3139 | 10609 A. (D2_L) | 11496 A. (D1-U) | 12277 A. (D2_L) | 12376 A. (D1_L) | 12833 A. (D1-L) |  | - | - | - | - |
| 8 | MBBL3407 | 11853.7 A. (D2_L) | 12123.9 A. (D2_U) | 12559.7 A. (D2_U) |  | - | - | - | - | - | - |
| 9 | MBBR3415 | 12402 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 10 | SSS272 | 11296.7 A. (QE-12) | 12581.7 A. (QE_34) | 12734 A. (QE-34) |  | - | - | - | - | - | - |
| 11 | MBAR1270 | 11809.3 A. (D1_L) | 12367 A. (D2-U) | 12839.4 A. (D2-L) |  | - | - | - | - | - | - |
| 12 | MBAL1072 | 11427.2 A. (D2_L) | 12741.5 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - |
| 13 | MBAL2209 | 11247.7 A. (D1_U) | 12532.6 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - |
| 14 | MBAR1264 | 11415 A. (D1-L) | 11894 A. (D1-U) | 12321.6 A. (D2-L) | 12531.6 A. (D2-L) |  | - | - | - | - | - |
| 15 | MBAL3395 | 12139.2 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - |

Long Connect time for SSS653 ;   Super good Noell Magnets at the end of their Series (3395, 3409,3415  :1 quench Ultimate )

3409 behaviour in 2nd run due to leak rather strange : dropped down  for 1st quench  to 11500 A after Ultimate reached in 1st run & the second run was  ON the BENCH  with warm up disconnection & Connection

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Thursday_01_A | TBA2 | Repair of the pumping valve of the CFB | ACR |  | No power test on test bench during the afternoon. |
| Tuesday_01_N | All | Cryo stop. All cold tests stopped. | ACR |  | General stop of the liquefactor. Stop 3 hours |
| Wednesday_02_A | TBC1 | No cold test can be launched because PLCSE was blocked. | ACR |  | Hardware reset done the OK. |
| Wednesday_02_N | TBC1, TBF1 | File not present in storage for C1 MBBL3407 .ka01 and F1 MBAR1264 .a03. | AB/CO |  | B Khomenko has been informed for correction. |
| Thursday_03_N | TBC2 | No signal using hfoff for Vcathode and Vanode on MB3407 during diode test. | MTM | hf | Signal found OK with lf off. |
| Friday_04_A | TBC2 | Problem in generating config.file for warm-up quench | MTM |  | Equip.support contacted. |
| Friday_04_A | TBC1 | MB3653 installed. No Temperature sensor attached in MTF | CRI |  | NC opened. HWREC put off. |
| Friday_04_A | TBA2 | MB2244: Quench during SPA test in the ramp down at 3700 A. | AB/PO? |  | Equip.support told to repeat the test. |
| Friday_04_A | TBE2 | HV CDBP on MB1255: test failed on Temperature sensor vs ground (5 A) instead of 2 A. The sensor still is working. | MTM |  | Equip.support checked the results and advised to open a NC. Test went on with Tsensor connected to have the recording with lf archiver during the run at cold. |
| Friday_04_A | TBC2 | MB2231: No diode bump observed during PTE. | MTM |  | Equip.support found that the cables to record the diode signals were not connected. He asked to repeat the test. Signal was then observed. |
| Friday_04_N | TBF2 | MB2244: Spike and noise seen in trigger & current signals of final warm-up quench. | MTM |  | Equipment support and TC contacted. TC asked to repeat the warm-up quench. |
| Friday_04_N | TBB1 | Triggers on potaim cards during IAP at warm on SSS261. | MTM |  | ICS has to check the connections. |
| Saturday_05_M | TBF1 | TEMA application blocked during IAP at warm | AB/CO |  | Crates reset. Then OK. |
| Saturday_05_M | TBE1 | SPA occurred during de-ramp of PT8 at around 5000A. Same during PT10. | MTM |  | D20 connector was found disconnected. |
| Sunday_06_A | TBB1 | SS261: On launching SPA test at 1000 A, the power converter is tripping when the current starts to ramp up from 50A. | AB/PO |  | Equip.support checked the faults and reset the power converter. |
| Sunday_06_A | TBC2 | Connection of the MB2241 cannot go on because magnet is not positioned properly. | ICS |  | ROCLA team did not answer to phone calls. Connection stopped up to Monday. |
| Sunday_06_A | TBC2 | Equip.support came to put HWREC on for tests of MB2241 (put off for the cold tests of MB3653) |  |  |  |
| Sunday_06_A | TBA2 | After warm up quench on MB3412 OP team signed the magnet on stand_by. Cryo team did not notice the message in the e-traveller and cool down the magnet again. | ACR |  | Warm up quench repeteated. |