### Chohan /14--Nov-05

### Week 46 starting  14 Nov 05

### SM18 Operation Meeting (Tuesdays)

Bench status on Monday 14 Nov 05:

11/14/2005 3:55:51 PM

| 9 | A1 |  |  | 295.18 |
| --- | --- | --- | --- | --- |
| 2 | A2 | MBAL3398 | Prep 5 Cool Down | 93.58 |
| 4 | B1 | SSS277 | PT 13.1 IAP @ Warm | 300.82 |
| 8 | B2 | SSS225 | ICS 2 Connect Magnet (ICS) | 294.1 |
| 7 | C1 | MBAR3328 | Prep 3 CDW1 HV | 292.94 |
| 5 | C2 | MBAL3414 | PT 12 Warm Up | 110.28 |
| 6 | D1 | SSS123 | PT 12 Warm Up | 128.42 |
| 12 | D2 | SSS193 | Prep 0 Scan Bench | 294.55 |
| 10 | E1 |  |  | 294.1 |
| 3 | E2 | MBBL2140 | Thermal Cycle | 271.02 |
| 11 | F1 | MBAL3139 | ICS 1 WP04 HV Test Warm | 292.94 |
| 1 | F2 | MBBR1281 | Prep 5 Cool Down | 79.29 |

Tempr. from TBSM18 site

Coordinator this week: John Miles; MTM support: 16-3602

16 complete Magnet Tests cycles  11 Dipoles  + 4 SSS + 1 SSSS

Disconnected or ROBTC after tests last week ( Sat Midnight to Sat midnight)

Situation From Cryogenics:  J-P Lamboy or ACR Rep.

Special Points:

- Sunday 13/11  Rocla : Not possible to change anymore magnets !

- Lot of piling up & magnets all cooling down  at same time Monday onwards

- Lots of Tests on SSS277 ?

- Tests Programme for 3139 ?

Special SSS Q6 on D2 (J Halik  , Marco)

AOB

| Magnets under Test from 06-11-2005 to 12-11-2005 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBBR3390 |  |  | 05-11-2005 | 38 h. | 18 h. | 15 h. | 13 h. | 25 h. | 09-11-2005 | 109 h. | Stripping |  |  |
| 2 | TBA2 | MBAL3412 |  |  | 04-11-2005 | 22 h. | 19 h. | 22 h. | 16 h. | 19 h. | 08-11-2005 | 98 h. | Stripping |  |  |
| 3 | TBA2 | MBAR2225 |  |  | 08-11-2005 | 26 h. | 21 h. | 24 h. | 17 h. | 11 h. | 12-11-2005 | 99 h. | Stripping |  |  |
| 4 | TBB1 | SSS261 |  |  | 04-11-2005 | 32 h. | 13 h. | 15 h. | 7 h. | 18 h. | 08-11-2005 | 85 h. | Stripping |  |  |
| 5 | TBB2 | SSS033 |  |  | 04-11-2005 | 33 h. | 16 h. | 16 h. | 9 h. | 17 h. | 09-11-2005 | 91 h. | Stripping |  |  |
| 6 | TBC1 | MBBL3653 |  |  | 04-11-2005 | 34 h. | 29 h. | 21 h. | 13 h. | 20 h. | 09-11-2005 | 117 h. | Stripping |  |  |
| 7 | TBC2 | MBAR2231 |  |  | 31-10-2005 | 58 h. | 26 h. | 26 h. | 13 h. | 11 h. | 06-11-2005 | 134 h. | Stand By |  |  |
| 8 | TBC2 | MBBR2241 |  |  | 06-11-2005 | 54 h. | 19 h. | 28 h. | 12 h. | 7 h. | 11-11-2005 | 120 h. | Stripping |  |  |
| 9 | TBD1 | SSS115 |  |  | 07-11-2005 | 44 h. | 14 h. | 19 h. | 7 h. | 12 h. | 11-11-2005 | 96 h. | Stripping |  |  |
| 10 | TBD1 | SSS218 |  |  | 01-11-2005 | 35 h. | 31 h. | 27 h. | 11 h. | 38 h. | 07-11-2005 | 142 h. | Stripping |  |  |
| 11 | TBD2 | SSS631 |  |  | 25-10-2005 | 72 h. | 71 h. | 198 h. | 11 h. | 13 h. | 09-11-2005 | 365 h. | Stand By |  |  |
| 12 | TBE1 | MBAR1273 |  |  | 02-11-2005 | 26 h. | 30 h. | 16 h. | 15 h. | 31 h. | 07-11-2005 | 118 h. | Stripping |  |  |
| 13 | TBE2 | MBAR1255 |  |  | 01-11-2005 | 37 h. | 35 h. | 35 h. | 17 h. | 13 h. | 07-11-2005 | 137 h. | Stripping |  |  |
| 14 | TBF1 | MBAR2248 |  |  | 04-11-2005 | 30 h. | 22 h. | 29 h. | 14 h. | 14 h. | 09-11-2005 | 109 h. | Stripping |  |  |
| 15 | TBF2 | MBAR2244 |  |  | 01-11-2005 | 29 h. | 30 h. | 23 h. | 15 h. | 19 h. | 07-11-2005 | 116 h. | Stripping |  |  |
| 16 | TBF2 | MBAR3376 |  |  | 07-11-2005 | 37 h. | 23 h. | 42 h. | 16 h. | 7 h. | 12-11-2005 | 125 h. | Stripping |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR3390 | 12614 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 2 | MBAL3412 | 11144.3 A. (D2_U) | 11305 A. (D1-U) | 12097.8 A. (D2-U) | 12395 A. (D1-L) | 12713.9 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - |
| 3 | MBAR2225 | 11973.3 A. (D2_L) | 12759.5 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | SSS261 | 12074 A. (QE-34) | 12421.9 A. (QI-34) | 12428.1 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS033 | 11755.7 A. (QI_34) | 12390.3 A. (QI_34) |  | - | - | - | - | - | - | - | - | - | - |
| 6 | MBBL3653 | 10386.7 A. (D1-U) | 11558.1 A. (D2-U) | 12153.6 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 7 | MBAR2231 | 10811.4 A. (D2_U) | 12032.3 A. (D2_U) | 12232.9 A. (D1-U) |  | - | - | - | - | - | - | - | - | - |
| 8 | MBBR2241 | 11721.5 A. (D2_L) | 12741.3 A. (D2-U) |  | - | - | - | - | - | - | - | - | - | - |
| 9 | SSS115 | 12139 A. (QI_12) | 12137 A. (QE-12) | 12464 A. (QE_12) |  | - | - | - | - | - | - | - | - | - |
| 10 | SSS218 | 12010 A. (QI_12) | 12477.3 A. (QE-12) | 12639 A. (QI-34) |  | - | - | - | - | - | - | - | - | - |
| 11 | SSS631 | 5422 A. (E_P12) | 5815 A. (E_P34) | 5820 A. | - | - | - | - | - | - | - | - | - | - |
| 12 | MBAR1273 | 12505 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 13 | MBAR1255 | 11547.6 A. (D1-U) | 12182.6 A. (D2_U) | 12457.3 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 14 | MBAR2248 | 11954.5 A. (D1_L) | 12792.3 A. (D1-L) | 12656 A. (D1-L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 15 | MBAR2244 | 10967.9 A. (D1_U) | 12520.7 A. (D2_U) | 12850 A. | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 16 | MBAR3376 | 12643 A. (D2_L_S01) | 12863 A. | - | - | - | - | - | - | - | - | - | - | - |  |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_08_A | TBF1 | MBAR 2248: TT821 reading during Powering tests is 1.552 K. So NC generated in CDW2. | MTM |  | MB was already warm. To react efficiently equip.support has to be called when the magnet is cold. |
| Wednesday_09_A | TBE1 | Polarity switch difficult to handle in left position. | MTM |  | Giorgio called and solved the problem. |
| Wednesday_09_N | TBC2 | Quench during the de-ramp of the current after SPA test at 12000A. | AB/PO |  | Report to AB/PO |
| Thursday_10_M | TBF2 | MM1 on MB3376:: MMP software does not recognise the magnet name. Unable to proceed with MM1. | AB/CO |  | Federico was informed. Problem solved. MMPvi was corrupted. |
| Thursday_10_A | TBF2 | Lost of cryo OK for all benches | ACR |  |  |
| Thursday_10_A | TBF2 | LHC cycle on MB3376 stopped because of a SPA. | ACR |  | Origin not known |
| Thursday_10_A | TBF2 | Ramp test launched. Stopped because current reading through MMP is not working in Ap1 | AB/CO |  | Federico called and changed the DIGIO card. |
| Thursday_10_N | TBF2 | Cryo lost during LHC cycle. | ACR |  |  |
| Friday_11_M | TBA2 | MB2225: SPA occurred during the plateau at 12850 A before generating the u_file. | AB/PO |  | Origin not knownTest will be repeated. |
| Friday_11_A | TBE1 | Quench during PT8 performed on MB2179 | AB/PO |  | TC noticed that this test was performed in the first run so he advised to proceed with the tests. |
| Friday_11_N | TBF2 | ROCLA parked in front of the bench impeded ICS team too remove the shafts from MB3376 | ICS |  | ICS team tried to contact ROCLA team. |
| Friday_11_N | TBB1 | Quench on SSS277: TC asked to perform 2 quenches at 2.3 K | AB/CO |  | ACR team answered that it is not possible at this temperature. |
| Saturday_12_A | TBE2 | During de-ramp of the current on MB2140 after PT8 quench at 1340 A. | AB/PO |  | Tripping of the power supply? TC decided to repeat the test. |
| Saturday_12_A | TBD2 | The Heat Sink of the Orbit Dipole connector no. 4 is bent - BEFORE connection by OP! |  |  |  |
| Sunday_13_N | TBD1 | SSS123: Signal for the external resistor QH3 is displayed flat from hfoff (AQA QH viewer). Signal are OK from lf application | AB/CO? | Hf (AQA) | Federico advised to proceed with the tests. |
| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| Tuesday_08_A | TBF1 | MBAR 2248: TT821 reading during Powering tests is 1.552 K. So NC generated in CDW2. | MTM |  | MB was already warm. To react efficiently equip.support has to be called when the magnet is cold. |
| Wednesday_09_A | TBE1 | Polarity switch difficult to handle in left position. | MTM |  | Giorgio called and solved the problem. |
| Wednesday_09_N | TBC2 | Quench during the de-ramp of the current after SPA test at 12000A. | AB/PO |  | Report to AB/PO |
| Thursday_10_M | TBF2 | MM1 on MB3376:: MMP software does not recognise the magnet name. Unable to proceed with MM1. | AB/CO |  | Federico was informed. Problem solved. MMPvi was corrupted. |
| Thursday_10_A | TBF2 | Lost of cryo OK for all benches | ACR |  |  |
| Thursday_10_A | TBF2 | LHC cycle on MB3376 stopped because of a SPA. | ACR |  | Origin not known |
| Thursday_10_A | TBF2 | Ramp test launched. Stopped because current reading through MMP is not working in Ap1 | AB/CO |  | Federico called and changed the DIGIO card. |
| Thursday_10_N | TBF2 | Cryo lost during LHC cycle. | ACR |  |  |
| Friday_11_M | TBA2 | MB2225: SPA occurred during the plateau at 12850 A before generating the u_file. | AB/PO |  | Origin not knownTest will be repeated. |
| Friday_11_A | TBE1 | Quench during PT8 performed on MB2179 | AB/PO |  | TC noticed that this test was performed in the first run so he advised to proceed with the tests. |
| Friday_11_N | TBF2 | ROCLA parked in front of the bench impeded ICS team too remove the shafts from MB3376 | ICS |  | ICS team tried to contact ROCLA team. |
| Friday_11_N | TBB1 | Quench on SSS277: TC asked to perform 2 quenches at 2.3 K | AB/CO |  | ACR team answered that it is not possible at this temperature. |
| Saturday_12_A | TBE2 | During de-ramp of the current on MB2140 after PT8 quench at 1340 A. | AB/PO |  | Tripping of the power supply? TC decided to repeat the test. |
| Saturday_12_A | TBD2 | The Heat Sink of the Orbit Dipole connector no. 4 is bent - BEFORE connection by OP! |  |  |  |
| Sunday_13_N | TBD1 | SSS123: Signal for the external resistor QH3 is displayed flat from hfoff (AQA QH viewer). Signal are OK from lf application | AB/CO? | Hf (AQA) | Federico advised to proceed with the tests. |