### Week 10 starting 6 March 06

### SM18 Operation Meeting (Tuesdays) 7 March 06

Bench status  on Monday  06-03- 2006 at:

| 5 | A1 | MBBR2299 | PT 6.4 Training 4 | 1.90 |
| --- | --- | --- | --- | --- |
| 12 | A2 | MBBL2142 | PT 14 Magnet MAPS | 299.56 |
| 4 | B1 | SSS216 | PT 8 Fast De-excitation | 1.90 |
| 10 | B2 | SSS085 | Prep 2.3 Res. Meas. CDW1 | 299.56 |
| 2 | C1 | SSS187 | PT 14 Magnet MAPS | 297.41 |
| 7 | C2 | SSS168 | PT 14 Magnet MAPS | 298.58 |
| 3 | D1 | SSS610 | PT 13.1 IAP @ Warm | 298.58 |
| 9 | D2 | SSS691 | ICS 5 Traveller Last | 298.58 |
| 1 | E1 | MBAR1321 | PT 14 Magnet MAPS | 300.82 |
| 8 | E2 | MBBR1309 | Prep 5 Cool Down | 211.94 |
| 6 | F1 | MBAR2234 | Prep 5 Cool Down | 93.26 |
| 11 | F2 | MBAR2247 | Prep 5 Cool Down | 288.83 |

3/6/2006 6:44:33 AM Tempr. from TBSM18 site

Supervisor: Stephane : Eq support : 16-3602 : Giogio

15 Magnet Tests completed :  6 Dipoles (1 with MM)

7 Arc-SSS,  2 IRSSS (With a thermal cycle)

General Points :

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- Situation from (SSS, SSSS)  :  J.Halik

- Special SSSS

- ICS : Magnet put on bench already tested (Dipole Magnet 1037 mounted on A1 by mistake by ICS).

- Equipment Support : a lot of error during IAP test (Maryline/Federico call last 2 weeks)

A.O.B.

# From 2/7/2006 to 2/13/2006

Tests Information

| Magnets under Test from 07-02-2006 to 13-02-2006 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBAL1065 |  | 30-01-2006 | 48 h. | 99 h. | 27 h. | 20 h. | 7 h. | 07-02-2006 | 201 h. | Stripping |
| 2 | TBA1 | MBAL1079 |  | 07-02-2006 | 31 h. | 24 h. | 31 h. | 18 h. | 20 h. | 13-02-2006 | 124 h. | Stripping |
| 3 | TBA2 | MBAL1081 |  | 06-02-2006 | 24 h. | 24 h. | 40 h. | 19 h. | 9 h. | 11-02-2006 | 116 h. | Stripping |
| 4 | TBB1 | SSS078 |  | 31-01-2006 | 47 h. | 71 h. | 42 h. | 10 h. | 7 h. | 07-02-2006 | 177 h. | Stripping |
| 5 | TBB1 | SSS169 |  | 08-02-2006 | 22 h. | 18 h. | 42 h. | 14 h. | 32 h. | 13-02-2006 | 128 h. | Stand By |
| 6 | TBB2 | SSS081 |  | 02-02-2006 | 47 h. | 23 h. | 64 h. | 10 h. | 18 h. | 09-02-2006 | 162 h. | Stripping |
| 7 | TBB2 | SSS146 |  | 09-02-2006 | 30 h. | 18 h. | 39 h. | 11 h. | 9 h. | 13-02-2006 | 107 h. | Stripping |
| 8 | TBC1 | SSS082 |  | 01-02-2006 | 100 h. | 13 h. | 26 h. | 6 h. | 18 h. | 08-02-2006 | 163 h. | Stripping |
| 9 | TBC1 | SSS211 |  | 08-02-2006 | 19 h. | 18 h. | 32 h. | 8 h. | 9 h. | 12-02-2006 | 86 h. | Stripping |
| 10 | TBC2 | SSS348 |  | 06-02-2006 | 38 h. | 18 h. | 19 h. | 7 h. | 10 h. | 10-02-2006 | 92 h. | Stripping |
| 11 | TBD1 | SSS608(2) |  | 03-02-2006 | 137 h. | 28 h. | 54 h. | 8 h. | 0 h. | 12-02-2006 | 227 h. | Thermal cycle |
| 12 | TBD2 | SSS619 |  | 30-01-2006 | 81 h. | 40 h. | 99 h. | 15 h. | 27 h. | 10-02-2006 | 262 h. | Stripping |
| 13 | TBE1 | MBAL1176 |  | 03-02-2006 | 42 h. | 70 h. | 39 h. | 20 h. | 19 h. | 11-02-2006 | 190 h. | Stripping |
| 14 | TBE2 | MBAL1083 |  | 31-01-2006 | 32 h. | 84 h. | 63 h. | 20 h. | 10 h. | 09-02-2006 | 209 h. | Stripping |
| 15 | TBF2 | MBAL2211 |  | 30-01-2006 | 52 h. | 94 h. | 155 h. | 19 h. | 15 h. | 13-02-2006 | 335 h. | Stripping |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1065 | 12584.2 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - |
| 2 | MBAL1079 | 12193 A. (D2_L) | 12803.7 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - |
| 3 | MBAL1081 | 10977 A. (D2_U) | 11356 A. (D2_U) | 11777 A. (D2_U) | 12106.9 A. (D2_U) | 12393 A. (D2-U) | 12669.6 A. (D2-U) | 12760.2 A. (D1_U) | 12818.8 A. (D2-L) | 12850 A. | - |
| 4 | SSS078 | 9902 A. (Vbus Int) | 9814 A. (Vbus Int) | 11998 A. (QI-34) | 12463.1 A. (QE-34) | 12633.9 A. (QE_12) |  | - | - | - | - |
| 5 | SSS169 | 11522.4 A. (QE_12) | 11702.3 A. (QE_12) | 11994.7 A. (QE_12) | 12127 A. (QE_12) | 12667.2 A. (QE_12) | 12648.9 A. (QI_12) | 12835.9 A. (QI-12) | 12851 A. | - | - |
| 6 | SSS081 | 12019.4 A. (QI_34) | 12252 A. (QI-12) | 12142 A. (QI-12) |  | - | - | - | - | - | - |
| 7 | SSS146 | 11871.2 A. (QI_34) | 12015.4 A. (QI_34) |  | - | - | - | - | - | - | - |
| 8 | SSS082 | 12314 A. (QI_34) | 12500.4 A. (QE_34) | 12782.6 A. (QE-12) |  | - | - | - | - | - | - |
| 9 | SSS211 | 11987.9 A. (Qe_34) | 12614.6 A. (QE-34) | 12850 A. | - | - | - | - | - | - | - |
| 10 | SSS348 | 12514.8 A. (QE_34) | 12728.1 A. (QE_12) | 12811.1 A. (QI-12) |  | - | - | - | - | - | - |
| 11 | SSS608 | 3283 A. (MI-2) | 3451 A. (MI-1) | 3494 A. (ME-1) | 3432.2 A. (M-E-I) | 3454.1 A. (M-E-2) | 3553.2 A. (M-E-1) | 3605.3 A. (MQ_E_1) | 3592.1 A. (MQ_I_1) | 3662.6 A. (MQ-I-2) | 3700.1 A. (MQ-I_2) |  |
| 12 | SSS619 | 4202 A. (MQM-E-34) | 4354 A. (MQ-E-1-2) | 4576 A. (MQ-E-34) | 4365 A. (Ext MQML) | 4650 A. | - | - | - | - | - |  |
| 13 | MBAL1176 | 11610.5 A. (D1_L) | 12163 A. (D1-L) | 12401.9 A. (D1-L) |  | - | - | - | - | - | - |  |
| 14 | MBAL1083 | 12311.8 A. (D2_U) | 12718.8 A. (D2-U) | 12850 A. (No Data) |  | - | - | - | - | - | - |  |
| 15 | MBAL2211 | 10292.7 A. (D1_L) | 11879.9 A. (D1-U) | 11880 A. (D1_L) | 12617.9 A. (D2_U) | 12850.2 A. (D2-U) | 12850 A. | - | - | - | - |  |

Problems on 2211  -  Long Magnetic measurment