### Week 26 starting 26 June 06

### SM18 Operation Meeting (Tuesdays) 27 June 06

Bench status  on Monday  25-06-2006 at:  6/25/2006 8:51:10 AM

8 A1 MBBR2303 Prep 5 Cool Down 1.90 12 A2 MBBL1390 ICS 4 Final connection 300.73 1 B1 SSS319 PT 9 CDAP HV 1.90 9 B2 SSS502 PT 3 QH Measure 1.90 10 C1 SSS271 ICS 3 Traveller after warm test 299.65 5 C2 SSS097 PT 13.2 Resist. Meas. 298.04 4 D1 SSSS634 PT 6.5 Training 5 4.62 HV 7 D2 SSS656 Prep 5 Cool Down 168.81 2 E1 MBAR1389 PT 13.2 Resist. Meas. 301.89 6 E2 MBBR1277 PT 12 Warm Up 150.78 3 F1 MBAR1352 PT 13.2 Resist. Meas. 300.28 11 F2 MBAR1292 PT 14 Magnet MAPS 300.37

CONFIG :  D6- AS3 –IRSSS3;

Supervisor: SANFILIPPO Stephane/

Eq support (Maryline till Friday and Guy Sat/Sun) : 16-3602 :

14 Magnet Tests completed : 8 Dipoles (), 4 Arc-SSS  ( 319 Go for Thermal cycle, )

(14 Magnets in all)		1  500-series ( 532 after Thermal cycle

2  600-series [ 678 (113 hrs),  659 (240  hrs), ]

General Points :

- Alarms on shaft, proposition of sent SMS directly to MTM piquet, for Croy and MTM diagnostic.

- Corrector analyze with AQA application.

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- News /Situation from (SSS, SSSS)  :  J Halik

- Situation SSSS  :OP issues :

- A.O.B..

# From 6/18/2006 to 6/24/2006

Tests Information

| Magnets under Test from 18-06-2006 to 24-06-2006 |
| --- |
| - | Bench | Magnet | Shafts | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |
| 1 | TBA1 | MBBR2290 |  | 09-06-2006 | 32 h. | 34 h. | 218 h. | 16 h. | 27 h. | 22-06-2006 | 327 h. | Stand By |
| 2 | TBA2 | MBAL2335 |  | 10-06-2006 | 36 h. | 25 h. | 109 h. | 17 h. | 18 h. | 19-06-2006 | 205 h. | Stripping |
| 3 | TBA2 | MBAL2569 |  | 19-06-2006 | 33 h. | 29 h. | 25 h. | 19 h. | 18 h. | 24-06-2006 | 124 h. | Stripping |
| 4 | TBB1 | SSS319(2) |  | 14-06-2006 | 78 h. | 50 h. | 95 h. | 7 h. | 0 h. | 23-06-2006 | 230 h. | Thermal cycle |
| 5 | TBB2 | SSS678 |  | 16-06-2006 | 38 h. | 17 h. | 23 h. | 14 h. | 21 h. | 21-06-2006 | 113 h. | Stand By |
| 6 | TBC1 | SSS136 |  | 19-06-2006 | 31 h. | 20 h. | 40 h. | 7 h. | 16 h. | 24-06-2006 | 114 h. | Stripping |
| 7 | TBC1 | SSS185 |  | 15-06-2006 | 31 h. | 14 h. | 33 h. | 13 h. | 11 h. | 19-06-2006 | 102 h. | Stripping |
| 8 | TBC2 | SSS340 |  | 17-06-2006 | 24 h. | 14 h. | 20 h. | 8 h. | 11 h. | 21-06-2006 | 77 h. | Stripping |
| 9 | TBD1 | SSS659 |  | 09-06-2006 | 30 h. | 21 h. | 121 h. | 9 h. | 59 h. | 19-06-2006 | 240 h. | Stand By |
| 10 | TBD2 | SSS532(2) |  | 15-06-2006 | 48 h. | 26 h. | 72 h. | 16 h. | 21 h. | 23-06-2006 | 183 h. | Stand By |
| 11 | TBE1 | MBAR1357 |  | 16-06-2006 | 30 h. | 20 h. | 22 h. | 15 h. | 22 h. | 21-06-2006 | 109 h. | Stripping |
| 12 | TBE2 | MBAR1300 |  | 16-06-2006 | 31 h. | 29 h. | 25 h. | 16 h. | 12 h. | 21-06-2006 | 113 h. | Stripping |
| 13 | TBF1 | MBBL2345 |  | 14-06-2006 | 26 h. | 40 h. | 22 h. | 14 h. | 19 h. | 19-06-2006 | 121 h. | Stripping |
| 14 | TBF2 | MBAR1320 |  | 13-06-2006 | 23 h. | 24 h. | 30 h. | 18 h. | 8 h. | 18-06-2006 | 103 h. | Stripping |

Quench Information

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR2290 | 11711.9 A. (D2_L) | 12437.4 A. (D1_U) | 12701.1 A. (D1_L) | 12850.4 A. (D1_L) | 12535.9 A. (D1_L) | 12514 A. (D1-L-S01) | 12622.6 A. (D1_U) | 12697.5 A. (D1_L) |  | - |
| 2 | MBAL2335 | 10698.4 A. (D2_L) | 12176.6 A. (D2-U) | 12253.9 A. (D1_L) |  | - | - | - | - | - | - |
| 3 | MBAL2569 | 11828 A. (D2-L) | 12537.5 A. (D2_L) | 12762 A. (D2_U) |  | - | - | - | - | - | - |
| 4 | SSS319 | 11575 A. (QE_12) | 11754 A. (QE_12) | 11862.7 A. (QI_34) | 11994.7 A. (QI-12) | 12088.7 A. (QI-12) | 12134.6 A. (QE_34) | 12161.6 A. (QE-34) | 12327.3 A. (QE-12) | 12516 A. (QI-12) | 12638.4 A. (QE-12) |  |
| 5 | SSS678 | 5109 A. (Ext_12) | 5470.3 A. (QI_12) | 5822 A. | - | - | - | - | - | - | - |  |
| 6 | SSS136 | 12803.7 A. (QI_12) | 12753.7 A. (QI_12) | 12679.6 A. (QI_12) | 12850 A. | - | - | - | - | - | - |  |
| 7 | SSS185 | 12070.8 A. (QI_34) | 12533.8 A. (QI_34) | 12850 A. (No Data) |  | - | - | - | - | - | - |  |
| 8 | SSS340 | 11520.6 A. (QE-12) | 12108.4 A. (QE-12) | 12423 A. (QE-34) |  | - | - | - | - | - | - |  |
| 9 | SSS659 | 3351.6 A. (MQY_12) | 3630.5 A. (I_MQY_34) | 3728.5 A. (E-MQY-34) | 3769.3 A. (MQY_I_34) | 3793.8 A. (I_MQY_12) | 3768.8 A. (MQY_I_34) | 3826.1 A. (I-MQY-12) | 3828 A. (I-MQY-12) | 3886 A. (MQY_I-12) | 3900 A. |  |
| 10 | SSS532 | 8749 A. (QI-12) | 8732 A. (QI-12) | 7524.7 A. (QI_12) | 11689.5 A. (QI_12) | 12600.5 A. (QE_34) | 12592.3 A. (QE_12) |  | - | - | - |  |
| 11 | MBAR1357 | 8078.6 A. (not det) | 12625 A. (D2_L) | 12703 A. (D2_U) | 12825.2 A. (D1_U) |  | - | - | - | - | - |  |
| 12 | MBAR1300 | 12281.4 A. (D1-U) | 12603.1 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - |  |
| 13 | MBBL2345 | 11733.4 A. (D2-U) | 12351.4 A. (D1-L) | 12705.2 A. (D2_L) |  | - | - | - | - | - | - |  |
| 14 | MBAR1320 | 12609 A. (D1_L) | 12705.8 A. (D1_L) | 12781.9 A. (D1_U) |  | - | - | - | - | - | - |  |

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuesday_20_M | TBB2 | SSS678: While doing PT 13.1 (IAP at WARM), errors are generated in MQML (Voltage taps). | MTM | IAP | Eq. support informed. OK to continue. IAP for MQTL not tune? |
| Tuesday_20_A | TBD2 | SSS532: Salem has informed that the SSW equipments should not be removed, and he will do the Chaconsa tests tomorrow 9 AM. He may be contacted for that. But during today night, the remaining corrector powering to be done: PT 5.5 and PT 5.6. The PT 5.4 is not successful as even nominal current (450A) could not be reached even after many attempts by him. | MTM |  | The magnet should be on 1.9 K till further message from Salem. |
| Tuesday_20_N | TBF2 | MB1292 : PT1 part1 (Tcoil) re-done. Offset adjustment on cards OK but the files made on 21th june are not readable using IAP. The date of 21/06 is not available! 2 files have been created: I0606210008.qc06 & 0022.qc07. | MTM | IAP | Equipment support will be informed to solve the problem tomorrow morning |
| Wednesday_21_M | TBF2 | MB1292: Training quench. Temperature shown as 1.9K but no cryo OK from Cryo team. Cryo team asked to wait for one hour. After one hour again it was asked to OP team to wait for 45 min. Subsequently Cryo team informed that there is cryo breakdown in F2.Problem in two Helium level sensors so cryo OK may not be possible | ACR |  | Stephane informed at 14h00 that the measurement is blocked. Stephane called the ACR on duty. Provisional reparation done at 15h00. Test could proceed. |
| Wednesday_21_A | TBD1 | SSS634: Problem with HV test on this S4: result not OK. | MTM |  | Salem found that one of the special adapters to be used for the HV test was not proper. He asked OP team to change it and redo the test and the results are found to be ok now. |
| Wednesday_21_A | TBD2 | SSS532 : HV test (PT9) on this SSS on D2 failed. Salem contacted. It was observed that Power converter was taken to CC in the conventional way with no ambiguity. PLCSE also shows PC in CC. But in reality it was found on top of CFB that it was not moved to CC from D2. | MTM |  | The PC switch was moved back and forth and the problem was solved. |
| Wednesday_21_A | TBB1 | SSS319 : MM1 was launched but not able to complete as Problem in Power supply access. Test tried 2-3 times | MTM |  | Equipment support informed. |
| Wednesday_21_N | TBB1 | SSS319: MMP does not recognize the TRU Position status, possibly due to a configuration problem. | MTM |  | Salem suggested that the expert should will have a look in the morning. |
| Wednesday_21_N | TBF2 | MB1292 : Results of MM2 shows orange alarm on multipoles at low current during ramp down at values close to 400 A. | MTM |  | MM2 validated. Switch to MM3. |
| Wednesday_21_N | TBF2 | MB1292: MM3 completed. OP team /Salem asked ICS to remove the shaft.. | MTM |  | No carriage available. MTM mechanics liberate one early in the morning. |
| Wednesday_21_N | TBB2 | SSS502: Clamp connection check. C/D potaim cards show a problem. Measurement on the C/D current leads showed open circuit whereas the documentation indicated a corrector on C/D. | MTM |  | ICS opened the manchette and corrected the connections, but the problem remained. Salem will investigate the problem in the morning. |
| Thursday_22_M | All | All control room TV screen are blank. No status display on TV screen. No automatic-updates on SMTMS. |  |  |  |
| Thursday_22_M | TBE2 | MB1277: Prep 2.1 launched from TEMA. Occurrence of an error message (Error in DB while executing Hr confgen). Federico checked the HWREC files, the name of the magnet was correct in MTF but the files generated by HWREC were displaying another magnet name.. | MTM | HWREC | Equipment Support contacted He suggested to check the MOBIC for entry. Entry found ok. Federico re-launched the HWREC process and the DB files were generated properly |
| Thursday_22_M | TBB1 | SSS319: Anticryostat alarm on aperture 1 since Wednesday afternoon.. Nobody informed. | ACR |  | Cable for temperature regulation disconnected by mechanical team to enter the long coils and not reconnected. T inside anti-cryostat up to 65 C. P. Legrand informed. Cable reconnected and helium flux send to lower the temperature. |
| Thursday_22_A | TBC1 | SSS136: QH power supply is not working. PLC fault dose not allow the tests to be launched from TEMA. | MTM |  | Federico contacted. He inspected and required time to rectify. Corrector powering is done from local station to save time. Federico swapped the QH3 power sources between A and C cluster. OK for cluster C power supply charging to 860V. The former power supply of C did not work even on A. This power supply is removed. P.Legrand will install a new one in A cluster. |
| Thursday_22_A | TBB2 | SSS502: Clamp connection check (Prep2.2C) could not be done. Constant LF trigger from card corresponding to CD corrector. | MTM |  | C/D still appears not to be connected in spite of a corrector specified in MTF. TC and equip. support should look into the problem in the morning. |
| Thursday_22_N | TBC1 | SSS136: The inductance value for PT1 was 62 mH by default TEMA settings. | MTM |  | It was then manually selected. |
| Friday_23_M | TBC1 | SSS136: MQ in C1 bench detrained by 50A during 2nd training, | MTM |  | A 3rd training would be launched as suggested by TC. |
| Friday_23_M | All | No cryo OK for benches F2 and B1. | ACR |  | Magnet 1292 is waiting for warm up quench. OK at 14h00 Magnet 1389 waiting for PT4. Ok at 16h00. |
| Friday_23_A | TBC1 | Video display is not functioning. |  |  |  |
| Friday_23_A | TBA1 | MB2303: QH power supply not working. | MTM |  | Equip. support called. He replaced the QH power supply. |
| Friday_23_A | TBB2 | SSS502: Problem with the CD Corrector settings, resulting in permanent trigger on LF. | ICS |  | Correction by ICS. |
| Friday_23_N Saturday_24_M | TBD1 | SSS634: Problem with the powering of KL circuit corrector. External_interlock. During KL MN powering the current was ramping to 80 A and then suddenly fall back to zero with no quench | MTM AB/PO |  | Equip. support called. Generator function is not working. Replaced with that of TBD2. Equip.support informed. The 120A Power supply on KL has not been reconnected properly last night (Wordfip) so it could not run. LF recording was not working due to a matrix trigger card that was not properly inserted in the chassis. The 120A Power supply on MN circuit is still not working, AB/PO eq.support has been called again, Solved by replacing the spare power supply by that of TBB. |
| Friday_23_N | TBD1 | SSS634: SSW roll angle measurement. Reading of the tension gives non correct value with the program. | MTM |  | OK with the command read_tension. OK with another DB file. Problem in the DB file? Guy checked Monady and found that all the config file from system 1 were copied in system 2. OK now. |
| Saturday_24_M | TBE2 | MB1277: Error in cryo phase during HV test.. | ACR |  |  |
| Saturday_24_A | TBD1 | SSS634: Problem of tension value during SSW measurements. | MTM |  | Federico called Guy. Software problem. Training quench done. SSW measurements done Monday. |
| Saturday_24_N | TBD1 | SSS634: Training of MQY could not be done. Main power converter (14KA) does not go to stand_by. Power application shows "Error 222 at check serial port" during execution of standby command from TEMA. | MTM |  |  |
| Sunday_25_M | TBB1 | SS319: TC inspects the performance of the magnet before giving OK for the warm_up. | MTM |  |  |
| Sunday_25_M | TBA1 | MB3203: ICS asked with shaft and TRU to be installed. | MTM |  | Federico contacted. He replied to use the usual pair and TRU. If problem he advised to contact the TC. |
| Sunday_25_M | TBD2 | MB3203: A table with computer from AB/PO is left in front of the bench blocking the access. | AB/PO |  | On monday morning the equip.support will come back to install the new generator function on the 120A PS for KL and MN correctors. |
| Sunday_25_A | TBA1 | MB2303: T_coil measurements give not correct values for some sectors. Some coils were showing high temp value (arround 400 deg K) when analysed from IAP T-coil | MTM |  | Calibration problems? Federico contacted. He advised to call stephane. Stephane advised to proceed with MM1, training MM2 and MM2. |
| Sunday_25_A | TBB1 | SSS319: Not possible to make the warm_up quench. A problem appeared when turning the PS on std-by, the first 3 potaim cards triggered. Stephane asked in any case to do a training quench as the performance is limit. | MTM |  | Federico checked the connections. Maybe a potaim card faulty? He advised to put the magnet on stand_by till Monday. Origin: adaptor was not removed after the HV test. |
| Sunday_25_N | TBE1 | MB1389. WP07 test failed MCS-MCD Correctors vs Ground. Leakage current marginally higher than safe value. Value of leakage current was consistent with three repeats. | MTM |  | Federico checked. Everything is OK from the measurement point of view. TC contacted Pierre for further investigation. Check by Richard Mompo. Test OK. |
| Sunday_25_N | TBB2 | SSS502. Powering of corrector circuits CD and EF could not be done. | AB/PO |  | Federico investigated with AB/PO support. Powering of CD could be done with a ramp rate 5 A/s that is the defined ramp rate. The power supply is still tripping for EF circuit. Solved by Jacky disconnecting and reconnecting the power converter. AB/PO will change the power converter. |
| Monday_26_M | TBA1 | MB3203: training quench : No LF data, warning in AQA | AB/CO | lf | TC asked to check in local sun. Giorgio found that the lf DAQ was blocked during the quench. Giorgio changed the power supply of the DAQ. |
| Monday_26_A | TBB2 | SSS502: MQTL training is very long (11 quenches and it did not reach ultimate. | MTM |  | TC decided to stop the training at 591 A. |
| Monday_26_A | TBE2 | MB1277: Vacuum leak found at cold by ACR team. Flexible repaired at warm | ACR |  | TC decided to coo down again the magnet for a leak test only. (magnet performance is OK). |
| Monday_26_A | TBD2 | SSS656: Not possible to power the magnet. | MTM |  | The wrong inductance was set in the main power converter (the one from previous magnet was there). |
| Monday_26_A | TBA1 | MB2303: Lf DAQ is not working. MM1: Overranges found in aperture 2 9sectors 2-3 and 12-13). | MTM |  | Maryline changed some cards. Stephane asked to investigate. |