### vc/Week 34 starting 21 aug 06

### SM18 Operation Meeting (Tuesdays) 22 Aug 06

Bench status  on Monday  14-08-2006 at 8/21/2006 1:57:48 PM

| 5 | A1 | MBAR2371 | PT 13.2 Resist. Meas. | 300.28 |
| --- | --- | --- | --- | --- |
| 10 | A2 | MBAR1322 | Prep 5 Cool Down | 76.06 |
| 3 | B1 | SSS318 | PT 6.4 Training 4 | 10.04 |
| 9 | B2 | SSS510 | PT 13.2 Resist. Meas. | 299.11 |
| 6 | C1 | SSS345 | ICS 4 Final connection | 296.25 |
| 11 | C2 | SSS140 | PT 13.1 IAP @ Warm | 293.65 |
| 7 | D1 | SSS660 | PT 6.7 Training 7 | 2.35 |
| 12 | D2 | SSS625 | PT 3 QH Measure | 1.90 |
| 4 | E1 | MBBR1367 | ICS 3 Traveller after warm test | 299.56 |
| 1 | E2 | MBBR2359 | Prep 5 Cool Down | 82.52 |
| 8 | F1 | MBAR2370 | PT 3 QH Measure | 2.35 |
| 2 | F2 | MBAR2274 | PT 6.6 Training 6 | 1.99 HV |

CONFIG :  D 6 - AS 3 -  IRSSS 3 ;

Supervisor:  Sandrine  ;Eq support : 16-3602

15 Magnet Tests completed (  )

8 Dipoles (2281 was Repeated but HV problem solved),

4 Arc-SSS  tests (303,304,   307 –ROBTC)

0  500-series [ ]

3  600-series [ 648 ( 190 hrs), 664 (136 hrs), 651 (210 hrs mech issues?) ]

General Points :

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- News /Situation from (SSS, SSSS)  :  J Halik

- Situation SSSS  :D1 & D2 issues; SSW, MM  & 660

  - Waiting for shafts for Monday on B2 510 from Sat afternoon

  - D1 660 SSW no program was given so OP initiative to do same as 648 (Q4) , no config file etc etc,

- A.O.B..

- Shutdown Next Year

WEEK 33

Benches A, C, E, F

Bench D

Bench B

| Magnets under Test from 13-08-2006 to 19-08-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBBR1308 |  |  | 07-08-2006 | 32 h. | 35 h. | 23 h. | 24 h. | 18 h. | 13-08-2006 | 132 h. | Stripping |  |  |
| 2 | TBA1 | MBBR2367 |  |  | 13-08-2006 | 23 h. | 23 h. | 21 h. | 19 h. | 16 h. | 17-08-2006 | 102 h. | Stripping |  |  |
| 3 | TBA2 | MBBR1307 |  |  | 14-08-2006 | 24 h. | 22 h. | 14 h. | 30 h. | 24 h. | 19-08-2006 | 114 h. | Stripping |  |  |
| 4 | TBA2 | MBBR1368 |  |  | 07-08-2006 | 41 h. | 24 h. | 48 h. | 21 h. | 14 h. | 14-08-2006 | 148 h. | Stripping |  |  |
| 5 | TBB1 | SSS304 |  |  | 11-08-2006 | 29 h. | 22 h. | 31 h. | 10 h. | 11 h. | 16-08-2006 | 103 h. | Stripping |  |  |
| 6 | TBB2 | SSS664 |  |  | 11-08-2006 | 45 h. | 39 h. | 17 h. | 9 h. | 26 h. | 16-08-2006 | 136 h. | Stand By |  |  |
| 7 | TBC1 | SSS303 |  |  | 09-08-2006 | 31 h. | 12 h. | 22 h. | 6 h. | 10 h. | 13-08-2006 | 81 h. | Stripping |  |  |
| 8 | TBC2 | SSS307 |  |  | 11-08-2006 | 29 h. | 16 h. | 59 h. | 7 h. | 0 h. | 16-08-2006 | 111 h. | Not Found or Thermal cycle |  |  |
| 9 | TBC2 | SSS307 |  |  | 16-08-2006 | 1 h. | 9 h. | 19 h. | 6 h. | 17 h. | 18-08-2006 | 52 h. | Stripping |  |  |
| 10 | TBD1 | SSS648 |  |  | 08-08-2006 | 53 h. | 19 h. | 98 h. | 9 h. | 11 h. | 16-08-2006 | 190 h. | Stand By |  |  |
| 11 | TBD2 | SSS651 |  |  | 09-08-2006 | 36 h. | 35 h. | 89 h. | 13 h. | 37 h. | 18-08-2006 | 210 h. | Stand By |  |  |
| 12 | TBE1 | MBBR2365 |  |  | 11-08-2006 | 39 h. | 30 h. | 19 h. | 12 h. | 7 h. | 16-08-2006 | 107 h. | Stripping |  |  |
| 13 | TBE2 | MBAR2373 |  |  | 14-08-2006 | 33 h. | 33 h. | 19 h. | 16 h. | 17 h. | 19-08-2006 | 118 h. | Stripping |  |  |
| 14 | TBE2 | MBBR2294 |  |  | 10-08-2006 | 26 h. | 33 h. | 19 h. | 16 h. | 17 h. | 14-08-2006 | 111 h. | Stripping |  |  |
| 15 | TBF1 | MBAL2281 |  |  | 10-08-2006 | 38 h. | 22 h. | 64 h. | 16 h. | 22 h. | 17-08-2006 | 162 h. | Stand By |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBBR1308 | 10076 A. (Vbus_Ext) | 12212.7 A. (D2_U) | 12640.6 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 2 | MBBR2367 | 11310.3 A. (D2_L) | 12346.8 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBR1307 | 11894.4 A. (D2-L) | 12768.9 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBR1368 | 12343.1 A. (D2_L) | 12433.8 A. (D2_L) | 12683 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS304 | 11479.3 A. (QI_34) | 12133.9 A. (QE_12) | 12303.8 A. (QE_12) |  | - | - | - | - | - | - | - | - | - |
| 6 | SSS664 | 5816.2 A. (E_MQML34) | 5822 A. | - | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS303 | 11395 A. (QI_12) | 12148 A. (QE_12) | 12322.7 A. (QE_34) |  | - | - | - | - | - | - | - | - | - |
| 8 | SSS307 | 10899.8 A. (QI_12) | 11709 A. (QE-34) | 11939.7 A. (QE_12) | 12077 A. (QI_12) | 12099.2 A. (QE_34) | 12392.1 A. (QE-12) | 12455.3 A. (QE_34) | 12508.9 A. (QE-12) | 12779.6 A. (QE_12) | 12697 A. (QE_12) |  | - | - |
| 9 | SSS307 | 12005.8 A. (QI_12) | 0 A. (No Data) | 12849.8 A. (QE_34) |  | - | - | - | - | - | - | - | - | - |
| 10 | SSS648 | 3512.9 A. (MQY_E_12) | 3577.4 A. (E_MQY_34) | 3591.2 A. (I_MQY_34) | 3662.9 A. (I_MQY_12) | 3710.6 A. (I_MQY_12) | 3730.2 A. (E_MQY_34) | 3770.5 A. (E_MQY_12) | 3793 A. (E_MQY_12) | 3879.4 A. (I_MQY_12) | 3810.9 A. (I_MQY_34) |  | - | - |
| 11 | SSS651 | 5739.4 A. (Ext_MQM1) | 5850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 12 | MBBR2365 | 11402 A. (D1_L) | 12166.9 A. (D1_U) | 12798 A. (D1-L) |  | - | - | - | - | - | - | - | - | - |
| 13 | MBAR2373 | 11193.4 A. (D1-U) | 12274 A. (D1_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 14 | MBBR2294 | 11412.4 A. (D1_L) | 11944.1 A. (D1_U) | 12449.4 A. (D1_U) | 12789.5 A. (D2-U) |  | - | - | - | - | - | - | - | - |
| 15 | MBAL2281 | 10025.9 A. (D2_L) | 11834.6 A. (D1_U) | 12488 A. (D1-U) | 12752 A. (D1-L) | 12798 A. (D1-U) | 12850 A. | - | - | - | - | - | - | - |

Back to Homepage | For print (Test/Quench/Graph)| For print (Waiting time\Disconnect time\Graph)

2281 leak & welding (overnight kept waiting); 651 had only 1 quench but cohabitation with 648 issues; 307 –ROBTC

CRYO SHUTDOWN PLANNING  FROM L.Serio @maric on 16 Aug 06

TS / AB coordination

- TS/CV has confirmed individual maintenance of PM18 cooling tower possible in // with 18kW run; will be performed between Dec 06 and Feb 07

- TS/CV requests 2 weeks maintenance SM18 cooling towers beginning of April

- TS/EL AUG tests (CERN 8.1;    point 1.8   29.3;    SM18 during first 2 weeks of April     )

- SPS cold checkout Feb-Mar 07; run from 2.4.07

- RF spare module tests at least until end of March 07

- Sector 1-2 cooldown 17.9.07

Run with 18 kW proposed until end of March 07

- Due to short commissioning time for cryo tunnel equipments in 2007, a mini-SD (already announced) is necessary on the 17.10.06 for 2 days (reduced cooling power with 6 kW)

- During Christmas SD the 18 kW is at nominal operating conditions for swift re-start of tests; if testing is required during this period we need to ask ALLS for additional support before end of September and identify CERN staff in addition to HC of LHC point 8

- 20 K cold compressors tests in Autumn 06

- Tunnel systems (QUI, QURC) validation Jan-Mar 07 in // with magnet testing

- SD April-June 07 for UNICOS upgrade + major overhauling

- Global validation and verification upgrade UNICOS + overhauling in July 07

- Preparation for HC August 07

Run with 6 kW proposed from 23.4.07

- Minimal maintenance on SM18 cryogenic installation during the first 2 weeks of April 07 (will run only 3 benches afterwards, i.e. parallel maintenance possible)

- Limited cooling power: coordination required (spare magnets, RF, other ?)