### VC/Week 36 starting 04sept 06

### SM18 Operation Meeting (Tuesdays) 05 sept 06

Bench status  on Monday  04-09-2006 at : 9/4/2006 9:58:17 AM

| 7 | A1 | MBBR2379 | Prep 5 Cool Down | 295.8 |
| --- | --- | --- | --- | --- |
| 4 | A2 | MBBR1369 | PT 12 Warm Up | 83.49 |
| 10 | B1 | SSS305 | PT 13.2 Resist. Meas. | 299.65 |
| 11 | B2 | SSS310 | PT 13.2 Resist. Meas. | 299.65 |
| 8 | C1 | SSS315 | ICS 4 Final connection | 298.67 |
| 6 | C2 | SSS346 | ICS 4 Final connection | 299.47 |
| 9 | D1 | SSS501 | PT 13.2 Resist. Meas. | 298.67 |
| 1 | D2 | SSS680 | PT5.4: Powering Corrector EF | 2.35 |
| 12 | E1 | MBAL1386 | ICS 1 WP04 HV Test Warm | 299.83 |
| 5 | E2 | MBAR2376 | PT 12 Warm Up | 203.71 |
| 3 | F1 | MBBR2360 | ICS 4 Final connection | 297.59 |
| 2 | F2 | MBBR1343 | PT 8 Fast De-excitation | 1.90 |

CONFIG :  D 6 - AS 3 -  IRSSS 3 ;

Supervisor:  nick  ;Eq support : guy+federico 16-3602

15 Magnet Tests completed (  )

8 Dipoles tests  ( “STAND BY” for 1346  9 ramp during for taining)

4 Arc-SSS  tests ( all stripped)

0  500-series []

3  600-series [ 665 (111 h), 662 (141 h) 667 (95 hr) ]

Sss241(C2), sss501(D1) , 1383(F1) were also finished early  Sat but not removed ( ICS pblms)

General Points:

- News /Situation  : D1 powering -giorgio

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- Situation SSSS  :D1 & D2 issues; Mechanics team Halik

- A.O.B..

## Tests

| Magnets under Test from 27-08-2006 to 02-09-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAL1403 |  |  | 28-08-2006 | 49 h. | 19 h. | 12 h. | 17 h. | 31 h. | 02-09-2006 | 128 h. | Stripping |  |  |
| 2 | TBA1 | MBAR2320 |  |  | 22-08-2006 | 23 h. | 23 h. | 16 h. | 15 h. | 35 h. | 27-08-2006 | 112 h. | Stripping |  |  |
| 3 | TBA2 | MBBR2316 |  |  | 24-08-2006 | 29 h. | 19 h. | 29 h. | 20 h. | 67 h. | 31-08-2006 | 164 h. | Stripping |  |  |
| 4 | TBB1 | SSS311 |  |  | 26-08-2006 | 28 h. | 12 h. | 14 h. | 7 h. | 58 h. | 31-08-2006 | 119 h. | Stripping |  |  |
| 5 | TBB2 | SSS665 |  |  | 22-08-2006 | 32 h. | 20 h. | 24 h. | 10 h. | 25 h. | 27-08-2006 | 111 h. | Stand By |  |  |
| 6 | TBC1 | SSS296 |  |  | 25-08-2006 | 27 h. | 15 h. | 12 h. | 7 h. | 17 h. | 28-08-2006 | 78 h. | Stripping |  |  |
| 7 | TBC1 | SSS331 |  |  | 28-08-2006 | 34 h. | 17 h. | 16 h. | 7 h. | 17 h. | 01-09-2006 | 91 h. | Stripping |  |  |
| 8 | TBC2 | SSS301 |  |  | 22-08-2006 | 32 h. | 18 h. | 15 h. | 7 h. | 73 h. | 28-08-2006 | 145 h. | Stripping |  |  |
| 9 | TBD1 | SSS662 |  |  | 23-08-2006 | 34 h. | 21 h. | 6 h. | 10 h. | 70 h. | 29-08-2006 | 141 h. | Stand By |  |  |
| 10 | TBD2 | SSS667 |  |  | 24-08-2006 | 31 h. | 14 h. | 18 h. | 10 h. | 22 h. | 28-08-2006 | 95 h. | Stand By |  |  |
| 11 | TBE1 | MBBR2369 |  |  | 26-08-2006 | 30 h. | 18 h. | 15 h. | 15 h. | 21 h. | 30-08-2006 | 99 h. | Stripping |  |  |
| 12 | TBE2 | MBAR1305 |  |  | 23-08-2006 | 36 h. | 19 h. | 12 h. | 14 h. | 12 h. | 27-08-2006 | 93 h. | Stripping |  |  |
| 13 | TBE2 | MBBR2332 |  |  | 27-08-2006 | 23 h. | 20 h. | 14 h. | 15 h. | 30 h. | 31-08-2006 | 102 h. | Stripping |  |  |
| 14 | TBF1 | MBAL1404 |  |  | 25-08-2006 | 26 h. | 19 h. | 14 h. | 19 h. | 20 h. | 29-08-2006 | 98 h. | Stripping |  |  |
| 15 | TBF2 | MBBR1346 |  |  | 23-08-2006 | 128 h. | 29 h. | 18 h. | 15 h. | 27 h. | 01-09-2006 | 217 h. | Stand By |  |  |

| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | MBAL1403 | 11725 A. (D2-U) | 11724 A. (D2_U) | 12640 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBAR2320 | 9808.8 A. (D2_U) | 12129.5 A. (D1_U) | 12852 A. | - | - | - | - | - | - | - | - | - | - |
| 3 | MBBR2316 | 11686.3 A. (D1_U) | 12649.9 A. (D1-L) | 12823.3 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 4 | SSS311 | 11608.4 A. (QE_12) | 12002.6 A. (QI_12) | 12457.6 A. (QI-12) |  | - | - | - | - | - | - | - | - | - |
| 5 | SSS665 | 5163 A. (IMQMLP12) | 5820 A. | - | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS296 | 10594.4 A. (QI_34) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 7 | SSS331 | 12131.2 A. (QE_34) | 12492.4 A. (QE-12) | 12602.5 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 8 | SSS301 | 10603.2 A. (QI_34) | 12317.3 A. (QE_!2) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 9 | SSS662 |  | - | - | - | - | - | - | - | - | - | - | - | - |
| 10 | SSS667 | 5424 A. (E_MQML12) | 5580 A. (E_MQML34) | 5820 A. | - | - | - | - | - | - | - | - | - | - |
| 11 | MBBR2369 | 11656 A. (D2_L) | 12667.3 A. (D1_L) | 12818.6 A. (D1-L) |  | - | - | - | - | - | - | - | - | - |
| 12 | MBAR1305 | 11373.5 A. (D1_U) | 12507.7 A. (D1_L) | 12800.9 A. (D1_U) |  | - | - | - | - | - | - | - | - | - |
| 13 | MBBR2332 | 11165.3 A. (D2_L) | 12147 A. (D1-U) | 12580 A. (D2-U) |  | - | - | - | - | - | - | - | - | - |
| 14 | MBAL1404 | 12508 A. (D2-L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 15 | MBBR1346 | 11780.1 A. (D1_U) | 12480.5 A. (D1_U) | 12770.4 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |

Long delays in 1346 connection ICS, long delays in ICS Disconnections :2316,301,311,2332,2320,1403

31/8/06/VC

The following EXPLAINS/shows/ proves that we have been seriously hampered by ICS non-availability to carry out the work in SM18 the last days of August. The majority yellow implies that … data collected here in 1 file since Aug 25th……see  below after the explanation

Some explanation

I have took the resume put in logbook of every shift of this week, and I have put the following color for each team :

………………… : CRYO

………………… : ICS

………………… : MTM

To understand :

that “PT13.2 in SMTMS” is “ICS task for E-traveller” (as for “ICS4 Final connection” in SMTMS is “CRYO task for e-traveller”)

( look up in SMTMS table and compared with e-traveller.)

When any of these type of tests are present on SMTMS it has already been done

_____________________________________________________________________________

[SM18 OP][COMMENT] 31/08/2006 21:19:21

[SM18 OP][COMMENT] 31/08/2006 21:00:00 Deshpande, Kaushik, Eric, Sheshnath 3 A1 MBAL1403 PT 12 Warm Up 10.26 11 A2 MBBR1369 Prep 0 Scan Bench 296.79 10 B1 SSS305 ICS 2 Connect Magnet (ICS) 296.34 9 B2 SSS310 Prep2.2C (CD clamp) 296.88 2 C1 SSS331 PT 12 Warm Up 294.73 5 C2 SSS241 PT 13.2 Resist. Meas. 296.07 7 D1 SSS501 Prep 5 Cool Down 4.96 HV 8 D2 SSS680 ICS 4 Final connection 295.8 6 E1 MBAL1399 ICS 4 Final connection 297.41 12 E2 MBAR2376 Prep 0 Scan Bench 296.7 4 F1 MBAL1383 Prep 5 Cool Down 1.93 1 F2 MBBR1346 PT 13.2 Resist. Meas. 298.58

[SM18 OP][COMMENT] 31/08/2006 13:00:00 Sunil k, Sampath, Kevin, Kuldeep. 3 A1 MBAL1403 PT 6.1 Training 1 4.26 HV 11 A2 MBBR2316 ICS 6 Disconnect Magnet WP07 295.62 10 B1 SSS311 PT 14 Magnet MAPS 295.8 9 B2 SSS310 Prep2.2C (EF clamp) 296.34 2 C1 SSS331 PT 9 CDAP HV 14.47 5 C2 SSS241 PT 13.2 Resist. Meas. 294.46 7 D1 SSS501 Prep 5 Cool Down 165.4 8 D2 SSS680 Prep 2.3 Res. Meas. CDW1 296.34 6 E1 MBAL1399 ICS 4 Final connection 296.88 12 E2 MBBR2332 PT 13.2 Resist. Meas. 296.07 4 F1 MBAL1383 Prep 5 Cool Down 95.05 1 F2 MBBR1346 PT 12 Warm Up 268.44

[SM18 OP][COMMENT] 31/08/2006 06:00:00 Panda, Rama, Gilbert, FLO 3 A1 MBAL1403 Prep 5 Cool Down 4.29 HV 11 A2 MBBR2316 PT 13.2 Resist. Meas. 296.25 10 B1 SSS311 ICS 5 Traveller Last 296.88 9 B2 SSS310 Prep2.2C (EF clamp) 296.88 2 C1 SSS331 PT5.6: Powering Corrector IJ 1.9 5 C2 SSS241 PT 12 Warm Up 95.38 7 D1 SSS501 ICS 4 Final connection 295.18 8 D2 SSS680 Prep 3 CDW1 HV 295.89 6 E1 MBAL1399 ICS 4 Final connection 297.41 12 E2 MBBR2332 PT 13.2 Resist. Meas. 296.7 4 F1 MBAL1383 Prep 5 Cool Down 222.36 1 F2 MBBR1346 PT 12 Warm Up 131.89

[SM18 OP][COMMENT] 30/08/2006 21:00:00 Shimjith, Dalal, Jackie, Eric 5 A1 MBAL1403 Prep 5 Cool Down 181.62 8 A2 MBBR2316 PT 13.2 Resist. Meas. 295.62 11 B1 SSS311 PT 13.2 Resist. Meas. 296.88 9 B2 SSS310 ICS 2 Connect Magnet (ICS) 296.88 4 C1 SSS331 Prep 5 Cool Down 2.35 3 C2 SSS241 PT 6.1 Training 1 4.40 HV 12 D1 SSS501 Prep 2.2 IAP @ warm HF 295.54 7 D2 SSS680 Prep 3 CDW1 HV 295.89 10 E1 MBAL1399 ICS 2 Connect Magnet (ICS) 297.32 1 E2 MBBR2332 PT 13.2 Resist. Meas. 298.31 6 F1 MBAL1383 ICS 4 Final connection 295 2 F2 MBBR1346 PT 6.2 Training 2 2.77 HV

[SM18 OP][COMMENT] 30/08/2006 13:00:00 Sonnis, Deshpande, Kaushik, Kevin 5 A1 MBAL1403 CR 1 Leak Test 296.25 8 A2 MBBR2316 PT 13.2 Resist. Meas. 295.62 11 B1 SSS311 PT 13.2 Resist. Meas. 296.88 9 B2 SSS310 ICS 2 Connect Magnet (ICS) 296.88 4 C1 SSS331 Prep 5 Cool Down 87.2 3 C2 SSS241 Prep 5 Cool Down 1.9 12 D1 SSS501 Prep 1 Lyre Test 295 7 D2 295.89 10 E1 MBBR2369 PT 14 Magnet MAPS 296.79 1 E2 MBBR2332 PT 13.2 Resist. Meas. 300.01 6 F1 MBAL1383 ICS 3 Traveller after warm test 295 2 F2 MBBR1346 PT 5.2 1.5 KA Quench HF 1.9

[SM18 OP][COMMENT] 30/08/2006 12:16:21 Priorities were changed at 07:00AM A1-5, A2-8, B1-11, B2-9, C1-4, C2-3, D1-12, D2-7, E1-10, E2-1, F1-6, F2-2

[SM18 OP][COMMENT] 30/08/2006 06:30:22 A1 MBAL1403 ICS 4 Final connection 296.52 A2 MBBR2316 PT 13.2 Resist. Meas. 296.43 B1 SSS311 PT 13.2 Resist. Meas. 296.88 B2 296.88 C1 SSS331 Prep 5 Cool Down 295.18 C2 SSS241 Prep 5 Cool Down 70.38 D1 SSS501 ICS 2 Connect Magnet (ICS)295.54 D2 295.89 E1 MBBR2369 PT 13.2 Resist. Meas. 298.04 E2 MBBR2332 PT 12 Warm Up 245.38 F1 MBAL1383 ICS 2 Connect Magnet (ICS)295.18 F2 MBBR1346 Prep 5 Cool Down 1.9

[SM18 OP][COMMENT] 29/08/2006 13:00:00 Jackie, Seshnath, Eric, Sampath 5 A1 MBAL1403 ICS 1 WP04 HV Test Warm 296.79 2 A2 MBBR2316 PT 13.2 Resist. Meas. 296.88 6 B1 SSS311 PT 13.2 Resist. Meas. 297.41 7 B2 SSS501 Bench under repair 296.88 8 C1 SSS331 Prep 2.2 IAP @ warm HF 295.8 9 C2 SSS241 ICS 3 Traveller after warm test 296.34 3 D1 SSS662 PT 14 Magnet MAPS 296.07 1 D2 296.43 10 E1 MBBR2369 PT 12 Warm Up 286.87 4 E2 MBBR2332 PT 6.1 Training 1 1.93 11 F1 MBAL1404 ICS 5 Traveller Last 296.88 12 F2 MBBR1346 Prep 5 Cool Down 138.88

[SM18 OP][COMMENT] 29/08/2006 06:00:00 Deshpande,Sonnis, Kevin, Swamy 5 A1 MBAL1403 ICS 1 WP04 HV Test Warm 296.79 2 A2 MBBR2316 PT 13.2 Resist. Meas. 298.04 6 B1 SSS311 PT 13.2 Resist. Meas. 298.04 7 B2 SSS501 Prep 0 Scan Bench 296.88 8 C1 SSS331 Prep 3 CDW1 HV 295.8 9 C2 SSS241 Prep 3 CDW1 HV 296.34 3 D1 SSS662 PT 13.2 Resist. Meas. 296.07 1 D2 296.43 10 E1 MBBR2369 PT 12 Warm Up 163.03 4 E2 MBBR2332 Prep 5 Cool Down 3.66 HV 11 F1 MBAL1404 PT 13.2 Resist. Meas. 298.04 12 F2 MBBR1346 Prep 5 Cool Down 291.78

[SM18 OP][COMMENT] 28/08/2006 21:00:00 Dixit, Patil, GHH,Padma 5 A1 MBAL1403 Prep 0 Scan Bench 296.79 2 A2 MBBR2316 PT 13.1 IAP @ Warm 298.04 6 B1 SSS311 PT 12 Warm Up 262.41 7 B2 SSS501 Prep 0 Scan Bench 296.88 8 C1 SSS331 Prep 0 Scan Bench 295.8 9 C2 SSS241 ICS 2 Connect Magnet (ICS) 296.34 3 D1 SSS662 PT 13.2 Resist. Meas. 296.7 1 D2 296.43 10 E1 MBBR2369 PT 8 Fast De-excitation 1.9 4 E2 MBBR2332 Prep 5 Cool Down 144.49 11 F1 MBAL1404 PT 12 Warm Up 286.87 12 F2 MBBR1346 Cryo problem 296.25

[SM18 OP][COMMENT] 28/08/2006 13:00:00 tikaria,sampath,eric,jackie 5 A1 MBAL1403 Prep 0 Scan Bench 296.79 2 A2 MBBR2316 PT 12 Warm Up 189.76 6 B1 SSS311 PT 8 Fast De-excitation 1.9 7 B2 SSS501 Prep 0 Scan Bench 296.88 8 C1 SSS296 PT 14 Magnet MAPS 295.8 9 C2 SSS241 Prep 0 Scan Bench 296.34 3 D1 SSS662 PT 13.2 Resist. Meas. 296.7 1 D2 SSS667 Finished Ready to go Final scan 296.43 10 E1 MBBR2369 PT 5.2 1.5 KA Quench HF 2.01 HV 4 E2 MBBR2332 Prep 5 Cool Down 296.25 11 F1 MBAL1404 PT 12 Warm Up 184.96 12 F2 MBBR1346 Cryo problem 296.25

[SM18 OP][COMMENT] 28/08/2006 06:00:00 Sonnis, Kevin, Dalal, Sunil K 5 A1 297.86 2 A2 MBBR2316 PT 12 Warm Up 13.25 6 B1 SSS311 PT5.6: Powering Corrector IJ 1.9 7 B2 SSS501 Prep 0 Scan Bench 297.41 8 C1 SSS296 PT 13.2 Resist. Meas. 295.18 9 C2 SSS301 PT 14 Magnet MAPS 296.88 3 D1 SSS662 Cryo problem 295 1 D2 SSS667 PT 14 Magnet MAPS 297.59 10 E1 MBBR2369 Prep 5 Cool Down 84.94 4 E2 MBBR2332 ICS 4 Final connection 297.32 11 F1 MBAL1404 PT 12 Warm Up 59.13 12 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 27/08/2006 21:00:00 Shimjith, Rama, Kulkarni, Sinha 5 A1 297.32 2 A2 MBBR2316 PT 8 Fast De-excitation 1.9 6 B1 SSS311 Prep 5 Cool Down 17.47 7 B2 SSS501 Prep 0 Scan Bench 297.41 8 C1 SSS296 PT 12 Warm Up 88.57 9 C2 SSS301 PT 14 Magnet MAPS 296.88 3 D1 SSS662 Cryo problem 294.46 1 D2 SSS667 PT 13.2 Resist. Meas. 298.04 10 E1 MBBR2369 Prep 5 Cool Down 237.23 4 E2 MBBR2332 Prep 3 CDW1 HV 298.04 11 F1 MBAL1404 PT 6.1 Training 1 3.55 HV 12 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 27/08/2006 13:00:00 Bakhtsingh, Deshpande, GHH, Patil 5 A1 296.79 2 A2 MBBR2316 PT 6.1 Training 1 1.9 6 B1 SSS311 ICS 4 Final connection 295.98 7 B2 296.88 8 C1 SSS296 PT 6.1 Training 1 3.24 HV 9 C2 SSS301 PT 13.2 Resist. Meas. 296.34 3 D1 SSS662 Cryo problem 293.83 1 D2 SSS667 PT 12 Warm Up 295.18 10 E1 MBBR2369 ICS 4 Final connection 297.86 4 E2 MBBR2332 ICS 1 WP04 HV Test Warm 298.04 11 F1 MBAL1404 PT 3 QH Measure 1.91 12 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 27/08/2006 09:12:45 The Magnet MBAR 2274 was put on TBA1. In consultation with TC, the ICS team was asked to remove the magnet from bench.

[SM18 OP][COMMENT] 27/08/2006 06:00:00 Padma,Seshnath,Panda, Kaushik 5 A1 MBAR2320 PT 14 Magnet MAPS 297.32 2 A2 MBBR2316 PT 5.2 1.5 KA Quench HF 1.9 6 B1 SSS311 ICS 3 Traveller after warm test 296.52 7 B2 SSS665 PT 14 Magnet MAPS 296.88 8 C1 SSS296 Prep 5 Cool Down 2.31 HV 9 C2 SSS301 PT 13.2 Resist. Meas. 296.34 3 D1 SSS662 Cryo problem 293.3 1 D2 SSS667 PT 12 Warm Up 15.67 10 E1 MBBR2369 ICS 4 Final connection 297.86 4 E2 MBAR1305 PT 13.2 Resist. Meas. 299.11 11 F1 MBAL1404 Prep 5 Cool Down 95.7 12 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 26/08/2006 21:00:00 Rama, Shimjith, Swamy, Kulkarni. 5 A1 MBAR2320 PT 13.2 Resist. Meas. 297.86 2 A2 MBBR2316 PT 1 IAP @ cold 1.9 6 B1 SSS311 Prep2.2C (CD clamp) 297.41 7 B2 SSS665 PT 13.2 Resist. Meas. 296.88 8 C1 SSS296 Prep 5 Cool Down 97.48 9 C2 SSS301 PT 13.2 Resist. Meas. 296.88 3 D1 SSS662 Cryo problem 292.23 1 D2 SSS667 PT 6.2 Training 2 1.91 10 E1 MBBR2369 Prep 1 Lyre Test 297.77 4 E2 MBAR1305 PT 12 Warm Up 294.64 11 F1 MBAL1404 Prep 5 Cool Down 280.27 12 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 26/08/2006 13:00:00 Deshpande, Patil, Bakhtsingh, GHH 12 A1 MBAR2320 PT 13.2 Resist. Meas. 297.86 3 A2 MBBR2316 Prep 5 Cool Down 95.62 11 B1 SSS311 Prep 0 Scan Bench 297.41 7 B2 SSS665 PT 13.2 Resist. Meas. 296.88 5 C1 SSS296 ICS 4 Final connection 295.89 10 C2 SSS301 PT 13.2 Resist. Meas. 296.88 6 D1 SSS662 PT 12 Warm Up 290.53 2 D2 SSS667 PT 5.2 1.5 KA Quench HF 1.91 9 E1 MBBR2369 ICS 1 WP04 HV Test Warm 297.77 1 E2 MBAR1305 PT 12 Warm Up 175.28 4 F1 MBAL1404 ICS 4 Final connection 295.89 8 F2 MBBR1346 Cryo problem 296.7

[SM18 OP][COMMENT] 26/08/2006 08:04:02 Priority changed 1- TBE2, 2- TBD2, 3- TBA2, 4- TBF1, 5- TBC1, 6- TBD1, 7- TBB2, 8- TBF2, 9- TBE1, 10- TBC2, 11- TBA1, 12- TBB1

[SM18 OP][COMMENT] 26/08/2006 06:00:00 Kaushik, Seshnath, Padma, Panda 1 A1 MBAR2320 PT 13.2 Resist. Meas. 299.02 7 A2 MBBR2316 Prep 5 Cool Down 242.06 8 B1 SSS318 ICS 5 Traveller Last 298.22 3 B2 SSS665 PT 13.2 Resist. Meas. 298.58 9 C1 SSS296 ICS 3 Traveller after warm test 296.97 2 C2 SSS301 PT 13.2 Resist. Meas. 297.41 6 D1 SSS662 PT 2 HV Cold Test 276.8 10 D2 SSS667 Prep 5 Cool Down 52.51 11 E1 MBBR1367 PT 14 Magnet MAPS 298.58 4 E2 MBAR1305 PT 9 CDAP HV 70.11 12 F1 MBAL1404 ICS 3 Traveller after warm test 296.43 5 F2 MBBR1346 ICS 4 Final connection 297.24

[SM18 OP][COMMENT] 25/08/2006 21:00:00 Tayade,Sampath,Swamy,Sunit Kulkarni 1 A1 MBAR2320 PT 13.2 Resist. Meas. 301.26 7 A2 MBBR2316 ICS 4 Final connection 297.41 8 B1 SSS318 PT 13.2 Resist. Meas. 298.22 3 B2 SSS665 PT 12 Warm Up 220.53 9 C1 SSS296 Prep2.2C (EF clamp) 297.59 2 C2 SSS301 PT 13.2 Resist. Meas. 296.88 6 D1 SSS662 Prep 5 Cool Down 4.75 HV 10 D2 SSS667 CR 1 Leak Test 296.97 11 E1 MBBR1367 ICS 6 Disconnect Magnet WP07 299.11 4 E2 MBAR1305 PT 4 Slow power abort check 2.24 HV 12 F1 MBAL1404 ICS 1 WP04 HV Test Warm 296.7 5 F2 MBBR1346 ICS 4 Final connection 298.31

[SM18 OP][COMMENT] 25/08/2006 13:00:00 Shimjith, GHH, Gupta, Deshpande 1 A1 MBAR2320 PT 12 Warm Up 261.8 7 A2 MBBR2316 ICS 4 Final connection 297.86 8 B1 SSS318 PT 13.2 Resist. Meas. 298.04 3 B2 SSS665 PT 6.1 Training 1 1.9 9 C1 SSS345 PT 14 Magnet MAPS 296.97 2 C2 SSS301 PT 13.2 Resist. Meas. 295.8 6 D1 SSS662 Prep 5 Cool Down 112.82 10 D2 SSS667 ICS 3 Traveller after warm test 296.97 11 E1 MBBR1367 PT 13.2 Resist. Meas. 298.58 4 E2 MBAR1305 Prep 5 Cool Down 95.05 12 F1 MBAR2370 PT 14 Magnet MAPS 296.07 5 F2 MBBR1346 ICS 4 Final connection 298.31

### MAGNET PRODUCTION SUMMARY FOR THE REFERENCE TASKS & PROCESSES BETWEEN 1/9/2006 AND 21/8/2006

| # | MAGNET | CFB | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1305 | E2 | 7h 12' | 3h 26' | 1h 25' | 2h 46' | 21h 0' | 39' | 11h 30' | 5h 27' | 1h 33' | 3h 36' | 8h 29' | 12h 17' | 11' | 14h 15' |
| 2 | 1322 | A2 | 8h 1' | 2h 18' | 1h 49' | 2h 53' | 9h 14' | 5h 38' | 14h 57' | 6h 52' | 1h 42' | 5h 4' | 13h 10' | 9' | 12h 15' | 1j 9h 44' |
| 3 | 1346 | F2 | 16h 7' | 2h 17' | 1h 48' | 3h 22' | 4j 8h 41' | 39' | 13h 39' | 4h 42' | 2h 10' | 14h 29' | 23h 7' | 10' | 12h 28' | 8h 49' |
| 4 | 1367 | E1 | 10h 47' | 2h 53' | 2h 7' | 2h 52' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 10' | 2j 8h 57' |
| 5 | 1369 | A2 | 7h 4' | 3h 14' | 49' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 6 | 1383 | F1 | 10h 17' | 5h 35' | 2h 26' | 3h 20' | 9h 18' | 39' | 12h 24' | 6h 15' | 1h 33' | 7h 51' | 10h 28' | 0' | 0' | 0' |
| 7 | 1399 | E1 | 4h 39' | 3h 14' | 1h 24' | 3h 35' | 18h 58' | 41' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 8 | 1403 | A1 | 17h 16' | 2h 29' | 2h 56' | 5h 44' | 9h 56' | 39' | 11h 40' | 4h 6' | 1h 52' | 4h 9' | 10h 29' | 10' | 8' | 0' |
| 9 | 1404 | F1 | 8h 26' | 2h 49' | 1h 23' | 2h 26' | 10h 39' | 39' | 11h 43' | 4h 42' | 2h 10' | 11h 0' | 15h 0' | 3h 45' | 12h 43' | 19h 21' |
| 10 | 2274a | F2 | 19h 18' | 3h 7' | 4h 3' | 5h 36' | 0' | 39' | 11h 43' | 0' | 0' | 11h 0' | 15h 0' | 3h 45' | 12h 43' | -12159' |
| 11 | 2316 | A2 | 6h 44' | 2h 40' | 3h 59' | 3h 30' | 11h 33' | 36' | 11h 54' | 4h 29' | 2h 3' | 21h 58' | 1j 4h 33' | 55' | 12h 41' | 2j 22h 8' |
| 12 | 2320 | A1 | 10h 19' | 1h 49' | 1h 16' | 1h 55' | 9h 35' | 43' | 13h 52' | 5h 35' | 1h 13' | 7h 16' | 12h 27' | 10' | 12h 7' | 1j 16h 42' |
| 13 | 2332 | E2 | 7h 11' | 1h 46' | 2h 11' | 1h 45' | 11h 20' | 12h 28' | 6' | 4h 11' | 1h 49' | 8h 22' | 14h 50' | 9' | 12h 32' | 1j 8h 48' |
| 14 | 2359 | E2 | 4h 33' | 4h 25' | 2h 12' | 2h 3' | 8h 54' | 1h 20' | 17h 47' | 10j 21h 21' | 0' | 0' | 0' | 0' | 0' | -12554' |
| 15 | 2369 | E1 | 8h 50' | 4h 13' | 2h 59' | 2h 45' | 10h 19' | 40' | 11h 26' | 5h 9' | 1h 30' | 10h 24' | 14h 31' | 9' | 12h 28' | 1j 0h 8' |
| 16 | 2370 | F1 | 4h 12' | 6h 0' | 1h 25' | 3h 31' | 12h 55' | 11h 21' | 14h 2' | 6h 46' | 2h 38' | 8h 7' | 10h 59' | 10' | 12h 23' | 1j 15h 21' |
| 17 | 2371 | A1 | 6h 26' | 4h 39' | 1h 20' | 2h 37' | 16h 11' | 4h 13' | 11h 45' | 4h 30' | 2h 4' | 13h 21' | 21h 53' | 11' | 12h 9' | 21h 14' |
| 18 | 2376 | A1 | 10h 33' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 19 | S140 | C2 | 9h 46' | 1h 47' | 1h 50' | 3h 36' | 6h 49' | 1h 6' | 4h 23' | 7h 20' | 2h 17' | 15h 1' | 22h 50' | 35' | 4h 18' | 19h 58' |
| 20 | s241 | C2 | 15h 37' | 3h 10' | 1h 1' | 7h 33' | 7h 3' | 1h 22' | 5h 59' | 4h 55' | 1h 36' | 9h 22' | 14h 9' | 10' | 4h 34' | 19h 29' |
| 21 | s296 | C1 | 8h 56' | 2h 0' | 1h 26' | 6h 30' | 6h 52' | 40' | 7h 0' | 3h 49' | 2h 36' | 10h 45' | 14h 30' | 10' | 4h 45' | 17h 14' |
| 22 | s301 | C2 | 13h 42' | 7h 0' | 1h 29' | 1h 50' | 8h 57' | 10h 51' | 6' | 3h 17' | 3h 33' | 11h 9' | 17h 30' | 11' | 4h 45' | 3j 2h 55' |
| 23 | s305 | B1 | 7h 56' | 2h 50' | 50' | 20' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 24 | s310 | B2 | 1j 8h 29' | 4h 31' | 54' | 3h 22' | 1h 46' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 25 | S311 | B1 | 10h 15' | 2h 8' | 2h 18' | 3h 59' | 6h 37' | 41' | 4h 39' | 3h 10' | 2h 41' | 10h 38' | 17h 5' | 10' | 4h 31' | 2j 15h 29' |
| 26 | s318 | B1 | 18h 18' | 2h 48' | 2h 26' | 2h 45' | 6h 53' | 39' | 4h 28' | 3h 18' | 2h 37' | 3j 18h 8' | 5j 0h 45' | 10' | 4h 59' | 2j 6h 3' |
| 27 | S331 | C1 | 8h 11' | 3h 7' | 1h 2' | 9h 36' | 13h 29' | 39' | 6h 11' | 11h 7' | 1h 21' | 5h 48' | 9h 36' | 10' | 4h 45' | 9h 38' |
| 28 | s345 | C1 | 13h 51' | 2h 57' | 2h 37' | 1h 56' | 9h 7' | 38' | 8h 30' | 2h 54' | 3h 23' | 10h 26' | 17h 39' | 10' | 5h 2' | 2j 1h 43' |
| 29 | S501 | B2 | 19h 32' | 12h 34' | 1h 13' | 1h 40' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| 30 | S510 | B2 | 11h 1' | 2h 22' | 1h 17' | 2h 47' | 8h 33' | 39' | 5h 25' | 2h 51' | 2h 36' | 1j 12h 15' | 1j 20h 27' | 26' | 5h 41' | 1j 5h 35' |
| 31 | S625 | D2 | 16h 48' | 3h 58' | 49' | 3h 50' | 11h 11' | 39' | 7h 39' | 4h 58' | 9h 0' | 1j 23h 6' | 2j 12h 14' | 10' | 7h 10' | 23h 41' |
| 32 | S660 | D1 | 5h 59' | 6h 25' | 20h 33' | 1h 1' | 8h 51' | 1h 26' | 9h 7' | 12j 14h 26' | 0' | 0' | 0' | 2h 19' | 5h 34' | 16h 58' |
| 33 | S662 | D1 | 7h 13' | 15h 25' | 2h 22' | 3h 41' | 7h 24' | 3h 55' | 6h 12' | 6h 10' | 6j 9h 16' | 0' | 1h 40' | 1h 58' | 6h 1' | 1j 3h 52' |
| 34 | s665 | B2 | 11h 38' | 2h 40' | 6h 1' | 3h 40' | 13h 16' | 43' | 7h 2' | 2h 16' | 7h 31' | 6h 27' | 1j 1h 52' | 5h 42' | 11' | 1j 19h 29' |
| 35 | S667 | D2 | 10h 28' | 7h 55' | 1h 27' | 6h 15' | 4h 12' | 39' | 7h 19' | 3h 20' | 2h 6' | 13h 13' | 18h 53' | 9' | 5h 49' | 1j 0h 10' |
| 36 | S680 | D2 | 23h 23' | 12' | 1h 36' | 2h 31' | 8h 24' | 39' | 0' | 0' | 0' | 0' | 0' | 0' | 0' | 0' |
| AVERAGES |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

### REFERENCE TASKS & PROCESSES

| 1 | CONNECTION ICS: (1.46¦1.45)-1.1 |
| --- | --- |
| 2 | WARM TEST: 2.4-(1.46¦1.45) |
| 3 | LEAK SEARCH ALLS: 3.3-2.4 |
| 4 | FERMETURE MANCHETTE ICS: 4.2-3.3 |
| 5 | POMPAGE VIDE OVC ALLS: Phase 5 |
| 6 | WAIT COOL DOWN: Phase 6 et FT265 inférieur à 40 g/s |
| 7 | COOL DOWN TO 80 K: Phase 6 et FT265 supérieur à 40 g/s |
| 8 | REMPLISSAGE LHe: Phase 9 |
| 9 | WAIT FIRST CRYO 1.9 [K]: CRYO 1.9 FLAG ON-Début Phase 10 |
| 10 | TOTAL CRYO 1.9 [K] OK TEST DURATION |
| 11 | TOTAL PHASE 10 DURATION (INCLUDING 9 & 10) |
| 12 | WAIT WARM-UP: Phase 13 et FT239 inf. 40 g/s |
| 13 | WARM-UP: Phase 13 et FT239 sup. 40 g/s |
| 14 | DECONNEXION ICS: 11.30 - Phase 16 |

OP Work Issues and MTF corrections Team excesses & diligence( A Tikaria)

These are the few and also quite similar common mistakes ( as stressed on the meeting on 15 Aug), observed during MTF correction and shift operation. This may help to improve our self.

1)       Corrector powering quench are many times not analysed by lfoff and uploaded on SMTMS.

2)       Uploading of HV file, CDPT file and CDR file but not updating the MTR.

3)       Some times uploading the wrong magnet file on the MTF.

4)       Wrong entry of currents of magnet training.

5)       Many time PT4 temperature not updated on the CDR files.

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Wednesday_30_M | TBF2 | MB1346 : HV (CDBP) failed for cold temp sensor Vs Ground (4 run recovery attempts made). | MTM |  | NC opened. Check by Richard. OK to continue. |
| Wednesday_30_M | TBD1 | SSS501: IAP at warm (HF heater discharge) could not be performed due to persistent triggers from Potaim cards V_clamp_ext and V_supra. | ICS |  | Richard was informed. Vtaps at the bottom of the main current leads (AB) are not connected. Richard asked ICS to open the big bellow. |
| Wednesday_30_M | TBF2 | MB1346 : PT5.2 (HF heater test at 1.5 kA) quench location is out of the magnel and warning HF-LF current discrepancy. | MTM | AQA | Richard advised further tests can be continued. |
| Wednesday_30_A | TBC2 | SSS241 : LF DAQ cannot be armed.. | AB/CO | lf | Lf DAQ finally OK after many resets of the sun station and crates. |
| Wednesday_30_A | TBE2 | MB1305 : Anomalous QH discharge on 3rd training. However, the magnet should be signed for standby. | AB/CO | AQA | Richard informed. He discussed with Boris: acquisition hardware problem. |
| Wednesday_30_N | TBD1 | SSS501 : Problem of offset for VT in the diode during IAP @ warm. Still no value. Anode and Cathode seems to be crossed. | MTM |  | Lemo cable for Int Diode was not connected Check will be done by Richard. |
| Wednesday_30_N | TBB2 | ICS informed us about connection cannot be finalized. They have try to move the magnet in connected position the metal pipe is too long. | MTM |  | ICS team leader informed us that previous magnet SSS501 went probably to D1 with the metal pipe of B2 bench. Magnet will be put in stand by till tomorrow. |
| Thursday_31_N Friday _01_M | all | Cryo Liquefactor problem. Problem to launch the training of MB1183. | ACR |  | OP team waited for the cryo clearance. |
| Friday_01_M | TBD1 | SSS501 : Problem of HF/LF DAQ not getting armed and magnet name disappeared from Tema, although name is showing in MTF . | MTM | HWREC | Richard informed. HWREC was not working because of the cohabitation with SSS681. HWREC must be switched off. |
| Friday_01_N | TBE2 | MB2376 : Temperature sensor reading is 119.8 K in place of 298 K. | MTM |  | Richard advised to proceed with the tests. NC opened. |
| Saturday_02_M | TBB2 | SSS310: TCLaux_X2 error reported by PLCSE. | MTM |  | Richard contacted. ACR have modified the level in the main current lead for quench in MQ. It perturbed the level in the auxiliary current lead. |
| Saturday_02_A | TBB2 | SSS310: SPA at 10428A TCL_X2 Fault. Problem Cryo |  |  |  |
| Saturday_02_A | TBB2 | SSS310: TCLaux_X2 error reported by PLCSE, again | MTM |  | ACR team changed the parameters. |
| Sunday_03_N | TBC2 | SSS346: IAP@warm. Alarms for Imax in the QH discharge (44A). QH resistances OK @ ~20 Ohm. It was observed that the Quench Heaters power supplies charge to >900V instead of ~850V. | MTM |  | Check by Richard. OK to continue. |
| Sunday_03_N | TBF2 | MBBR1343. During first training noise was observed on D2_U-L. However no noise was visible on direct voltage taps. | MTM |  | Check by TC? Giorgio has been consulted for the problem he suggested to continue. If again problem observed then it may me required to change the coresponding Potaim Card |
| Monday_04_M | TBF2 | MB1343: no LF data during second training quench. | MTM |  | Richard checked that some files were missing on the storage volume. He rectified the problem but it seems that HF and LF were not triggered exactly at the same time giving some warnings on AQA. Richard validated the quench. |
| Monday_04_A | TBC1 | SSS310: Flexible of the E-line was leaking | ACR |  | Repaired. |