### VC- /Week 42 starting 16 October 06

### SM18 Operation Meeting (Tuesdays) 17 Oct 06

Bench status  on sunday 15-oct-2006 at:

10/15/2006 9:21:48 PM

| 3 | A1 | MBBR2382 | ICS 4 Final connection | 297.15 |
| --- | --- | --- | --- | --- |
| 9 | A2 | MBBL1380 | Prep 4 TRU Connection | 1.90 |
| 8 | B1 | SSS518 | Cryo problem | 5.41 |
| 4 | B2 | SSS353 | PT 13.2 Resist. Meas. | 297.41 |
| 1 | C1 | SSS278 | Prep 3 CDW1 HV | 296.52 |
| 2 | C2 | SSS339 | ICS 6 Disconnect Magnet WP07 | 296.43 |
| 11 | D1 | SSS520 | PT5.4: Powering Corrector EF | 1.89 |
| 12 | D2 |  |  | 296.34 |
| 6 | E1 | MBBR2389 | PT 13.2 Resist. Meas. | 301.35 |
| 5 | E2 | MBBL2357 | PT 13.2 Resist. Meas. | 296.88 |
| 7 | F1 | MBBL1409 | PT 6.3 Training 3 | 10.18 |
| 10 | F2 | MBBL1408 | Cryo problem | 296.88 |

CONFIG :  D 6 - AS 4 -  IRSSS 2 ;

Supervisor:  stephane ;Eq support : 16-3602

14 Magnet Tests completed ( 5 Magnet Stripped )

08 Dipoles tests	()

5 Arc-SSS  tests (317 had long MM)

1  500-series (515 despite  ROBTC but did not reach 12KA in 2 quenches but…)

0  600-series [ ]

General Points:

- SSS339 & Q-loc not recorded in SMTMS

- Situation from Cryogenics:  J-P Lamboy or ACR Rep.

- Situation SSSS  :D1 & D2 issues J Halik

- A.O.B..

| Magnets under Test from 08-10-2006 to 14-10-2006 |
| --- |
| - | Bench | Magnet | Shafts | + | Start Date | Connect Time | Cooling Time | Cold Test Time | Warming Time | Disconnect Time | End Date | Total | Signed for |  |  |
| 1 | TBA1 | MBAL2336 |  |  | 05-10-2006 | 41 h. | 19 h. | 20 h. | 16 h. | 12 h. | 09-10-2006 | 108 h. | Stripping |  |  |
| 2 | TBA1 | MBBL1373 |  |  | 10-10-2006 | 40 h. | 22 h. | 17 h. | 16 h. | 16 h. | 14-10-2006 | 111 h. | Stripping |  |  |
| 3 | TBA2 | MBBR2390 |  |  | 03-10-2006 | 40 h. | 19 h. | 19 h. | 19 h. | 10 h. | 08-10-2006 | 107 h. | Stripping |  |  |
| 4 | TBA2 | MBBR2393 |  |  | 08-10-2006 | 32 h. | 22 h. | 21 h. | 15 h. | 6 h. | 12-10-2006 | 96 h. | Stripping |  |  |
| 5 | TBB1 | SSS145 |  |  | 06-10-2006 | 34 h. | 13 h. | 23 h. | 9 h. | 28 h. | 11-10-2006 | 107 h. | Stripping |  |  |
| 6 | TBB2 | SSS354 |  |  | 07-10-2006 | 0 h. | 9 h. | 11 h. | 11 h. | 30 h. | 10-10-2006 | 61 h. | Stripping |  |  |
| 7 | TBC1 | SSS358 |  |  | 06-10-2006 | 30 h. | 17 h. | 17 h. | 8 h. | 11 h. | 09-10-2006 | 83 h. | Stripping |  |  |
| 8 | TBC1 | SSS360 |  |  | 09-10-2006 | 39 h. | 20 h. | 18 h. | 8 h. | 37 h. | 14-10-2006 | 122 h. | Stand By |  |  |
| 9 | TBD1 | SSS317 |  |  | 29-09-2006 | 88 h. | 16 h. | 178 h. | 8 h. | 32 h. | 13-10-2006 | 322 h. | Stripping |  |  |
| 10 | TBD2 | SSS515 |  |  | 07-10-2006 | 0 h. | 16 h. | 13 h. | 12 h. | 26 h. | 10-10-2006 | 67 h. | Stand By |  |  |
| 11 | TBE1 | MBBR2387 |  |  | 06-10-2006 | 22 h. | 25 h. | 23 h. | 19 h. | 25 h. | 11-10-2006 | 114 h. | Stripping |  |  |
| 12 | TBE2 | MBBR2388 |  |  | 04-10-2006 | 53 h. | 21 h. | 20 h. | 18 h. | 34 h. | 10-10-2006 | 146 h. | Stripping |  |  |
| 13 | TBF1 | MBBR2381 |  |  | 07-10-2006 | 39 h. | 28 h. | 16 h. | 16 h. | 23 h. | 12-10-2006 | 122 h. | Stripping |  |  |
| 14 | TBF2 | MBBR2374 |  |  | 07-10-2006 | 73 h. | 19 h. | 15 h. | 17 h. | 26 h. | 13-10-2006 | 150 h. | Stripping |  |  |
| - | Magnet | Q1 | Q2 | Q3 | Q4 | Q5 | Q6 | Q7 | Q8 | Q9 | Q10 | Q11 | Q12 | Q13 |
| 1 | MBAL2336 | 11759 A. (D1_U) | 12327.6 A. (D2_L) | 12586.3 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 2 | MBBL1373 | 12005.3 A. (D1_L) | 12501.4 A. (D1_L) | 12666.8 A. (D1_L) |  | - | - | - | - | - | - | - | - | - |
| 3 | MBBR2390 | 10884 A. (D1_U) | 12383.9 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 4 | MBBR2393 | 11366.1 A. (D1_L) | 12407.1 A. (D1_U) | 12807.8 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - |
| 5 | SSS145 | 12368.7 A. (QE_12) | 12789.5 A. (QE_12) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 6 | SSS354 | 11704.6 A. (QI_12) | 11533.4 A. (No Data) | 12379.3 A. (QI_34) |  | - | - | - | - | - | - | - | - | - |
| 7 | SSS358 | 11058.5 A. (QE_12) | 11449.6 A. (QE_12) | 12633.4 A. (QE_12) | 12724.9 A. (QE_12) |  | - | - | - | - | - | - | - | - |
| 8 | SSS360 | 11607.5 A. (QI_12) | 12698.2 A. (QI_12) | 12816.2 A. (QE_12) |  | - | - | - | - | - | - | - | - | - |
| 9 | SSS317 | 10921.6 A. (QI_12) | 12561.5 A. (QE_34) | 12740.9 A. (QE_34) | 12846 A. (QE-12) | 12850 A. | - | - | - | - | - | - | - | - |
| 10 | SSS515 | 11309.8 A. (QI_12) | 11776.3 A. (QI_34) | 12167.3 A. (QI_12) |  | - | - | - | - | - | - | - | - | - |
| 11 | MBBR2387 | 12671.4 A. (D2_L) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 12 | MBBR2388 | 12136.9 A. (D2_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - | - |
| 13 | MBBR2381 | 11470.2 A. (D2_L) | 12820 A. (D1_U) | 12850 A. | - | - | - | - | - | - | - | - | - | - |
| 14 | MBBR2374 | 11048.5 A. (D1_L) | 12082.7 A. (D2_U) | 12411 A. (D2_L) |  | - | - | - | - | - | - | - | - | - |

LONG MM on SSS317

| Date | Bench | Problem | Type | Application/ soft | Action/advise |
| --- | --- | --- | --- | --- | --- |
| Tuedsay_10_N | TBC2 | SSS339 : After the first training quench alarms in AQA, signals not coherent. | MTM | AQA | Giorgio contacted. Problem coming from the changes induced by the shaft localization (channels shifted). Giorgio advised to create a dummy file without Q_loc and use it to analyse the quench. Giorgio corrected the configuration Wednesday morning. |
| Wednesday_11_M | TBD1 | SSS317 : During special LHC cycle, cryo OK lost, communication problem in ACR supervision | ACR |  | Test re-launched. |
| Wednesday_11_M | TBA2 | MB2393: No quench heater data was available after warm-up quench (training quench a03). | MTM |  | Guy advised to re-launch the warm-up quench. |
| Thursday_12_A | TBA2 | MB1380: Scanning of the magnet, pointer of the mobic not found. |  |  |  |
| Saturday_14_A | TBF2 | MB1408: Temperature anti-cryostats too low. | ACR |  | ACR team asked to ignore the alarm. |
| Sunday_15_M | TBB1 and TBF1 | SSS518, MB1409: Temperature on TBB1 and TBF1 was stuck at 4.5K. | ACR |  | Pumping system is not working properly. |
| Sunday_15_M | TBF | MB1408, MB1409: Significant temperature difference was observed between TT821 and TT147. | MTM |  | Guy contacted. |
| Sunday_15_A | TBB1 | SSS518: TCl_aux fault. | ACR |  | Sensor to be changed.. SSS warmed up, naturally sensor changed Monday and SSS cooled down again. |
| Sunday_15_A | TBF2 | MB1408: Big leak found in the magnet at warm. Vacuum broken by cryo. Problem with anti-cryostat. | MTM |  | Action ? Anti-cryostat cable was damaged in the aperture 1. OP team replaced this cable by one from A cluster. Salem has been informed. |
| Sunday_15_N | TBA2 | MB1380: Q_loc position different in the TRU between the two apertures. Switch adapted accordingly. | MTM |  |  |
| Sunday_15_N | TBF1 | MB1409.: Training quench, lf crate hanging. | AB/CO | lf | Lf crate re-started. |
| Monday_16_M | TBE1,TBA2 | EDMS upgrade: HWREC stopped. MM2 launching in MB1380 and upload of WP07on MB2389 delayed. | IT | EDMS |  |
| Monday_16_M | TBA2 | MB1380: MM2 checked by Stéphane. Two sectors in each aperture displaying wrong magnetic field | MTM |  | Stéphane asked Guy to check the measurement chain (Amplifiers, integrators.). |
| Monday_16_M | TBD1 | SSS320: MQTL powering, the magnet did not reach 600 A after 9 ramp. | MTM |  | Stéphane asked to continue the training up 550 A adding some quenches because magnetic measurements is required on this magnet. The MQTL reached 534 and then de-trained. Stéphane asked for 2 last quenches and stop. He will change the MM accordingly. |
| Monday_16_A | TBA2 | MB1380: At the end of MM3 (~1000 A) the current failed down. Slow PA, lost of cryo OK? Same problem happened during the test ramp | MTM |  | Stéphane validated the measurement. Giorgio informed. |