ATLAS Roman Pot Test Beam survival diary

To start DAQ :

- Open a window (if none is available) on pctbatl04p

  - if PC as to be restarted from scratch, account is “lumidaq” and password is “LumiDaq”

- type “run”

- set number of events in “run parameters”

- type “boot” and “configure”

- type “start” to start a run

- go to step 5 to start further new runs

To transfer data from DAQ PC to analysis PC

- Open a window (if none is available) on pctbatl04p

- scp /data/daq/DATAFILE.data lumidaq@pctb-pi-ros01:DAQ-data/

  - the requested password is “LumiDaq”

To launch analysis on a run

- Open a window (if none is available)

- cd Analysis_OnlyAlpha_DAQ

- source setup-ROOT.csh

- Translate binary file to ROOT file by typing “./readAlpha ../DATAFILE.data 5 n v”

- Start ROOT via “root –l”

- Load connectivity file by typing “.L testConnectivity.c”

- Check connectivity by typing “testConnectivity();”

- Load geometry file by typing “.L testGeometry.c”

- Perform analysis by typing “testGeometry();”

- Quit Root by typing “.q”

- Check plots created in folder PLOT

  - ggv PLOT/histHT.eps will display total number of hits per event

  - ggv PLOT/histHPL.eps will display number of hits per layer

  - ggv PLOT/xyDist.eps will display the XY distribution

To reset electronics (from PC in rack R29)

- Go to PVSS Console

- Stop all managers with red light

- Turn OFF low voltages power supplies

  - the 3 power supplies are located in the same rack, above the screen

- Turn ON low voltages power supplies after 2 s

- Start all managers (green light)

- On “Device Editor & Navigator” window, select “Logical” and “PMF setup”

- Loop on all 5 PMF :

  - Select PMF #

  - Set DAC value for threshold (4th parameter of “Mirror” column). Do not forget ENTER on keyboard

  - Press “Selected PMF” for gain and DAC

  - Wait for “Status” line to become green

  - Go to step a) for next PMF

- Turn OFF known noisy channel

  - Press “Launch interface” on “Manual commands” area

  - Write Chip = “00100”, Register=”000010” and Channel=”0000000100000000” (corresponding to Channel #14 of PMF #4) on “Write data” area

  - Press “Send command” on “Write data” area

  - Check the masked channel is the right one with on “Send command” on “Read data” area

  - Exit this window